## Slide 1: Crossroads - A Time-Sensitive Autonomous Intersection Management Technique
Edward Andert
Thesis Defense – January 12th 2017
Committee: Dr. Aviral Shrivastava, Dr. Georgios Fainekos, and Dr. Heni Ben Amor

## Slide 2: Autonomous Intersection Management
As cars become autonomous, so too can intersections
Why?
  683 died in vehicles crashes from running red lights in 2012 (NCSR)
  127,000 sustained injuries in 2012 (NCSR)
  Average person estimated to wait 6 months of their life at traffic lights (http://www.thefactsite.com/2010/03/how-much-time-people-spend-doing-stuff.html)
We must design an autonomous Intersection Manager (IM) such that the following criteria are met:
  Safe
  High Throughput
Notes: Inersection specific data only

## Slide 3: Testing Assumptions With Scale Model
“1/10 scale” model of an intersection
  System supports 8 vehicles.
  Vehicles are built on a Traxxas platform with Arduino Mega 2560 as a controller.
  Positioning is handled by quadrature encoder attached to motor.
  Network is handled by 2.4GHz transceivers.

## Slide 4: Scale Model Specifications
Single lane intersection
  = 1
  = .605 m
  = 3 m
  .568 m
  . 296 m
1
1
1
1
Request
Line
Request
Line
Request
Line
Request
Line

## Slide 5: Velocity Transaction Intersection Manager (VT-IM)
Method #1 (VT-IM) - A simple approach to scheduling cars in an intersection.

## Slide 6: Defining a Simple Intersection Manager
Vehicle reaches request line and transmits current speed and position
Vehicle receives new target velocity from IM.
We will call this a Velocity Transaction Intersection Manager or VT-IM.
1
1
1
1
Request
Line
Request
Line
Request
Line
Request
Line
Vt-im references
Notes: One way to implement, define charecteristics

## Slide 7: Demo VT-IM (Velocity Transaction Intersection Manager)
Intersection Manager
Request Line
Enter
Exit
3.0
2.5

## Slide 8: Demo VT-IM Code
Intersection Manager Code:
1 if(request received) {
AddVehicleToQueue();
= CalculateDesired ;
s;
5 }
Vehicle Code:
1 SendRequest(){ // Sends request to enter the IM
send [, , LI, DI, LO, DO]; // Position, Velocity, Lane of // Entry, Direction of Entry, Lane of Exit, Direction of exit
Receive ;
Set ; }
5 Interrupt(request line crossed){ // Received reply from IM
6 timeEapsed = 0; 7 SendRequest();
8 }
9 Interrupt(timeEapsed > timeout){ // Re-requests if no reply from IM
10 If( <= ){
11 = 0;
12 }
13 SendRequest(); }
Notes: More to algorithm, not present here for berevity

## Slide 9: VT-IM Must Account for Position Uncertainty
An intersection manager should take into account all kinds of errors and uncertainties in the system.
  Sensor Error
  Time Synchronization Error
  Control Error
Error is modelled as a Safety Buffer around the vehicle:

## Slide 10: How Large is the Safety Buffer
Using our real-life implementation, we measured how big a Safety Buffer needed to be.
  .568 m
    .15m @ , 12.6km/h

## Slide 11: Large Safety Buffer Lowers Throughput
Intersection Manager
Request Line
Enter
Exit

## Slide 12: Even with Safety Buffer, Accidents Will Still Happen
Despite adding in the Safety Buffer to our real implementation, we were still seeing crashes in fringe cases.
Notes: Accenturate Problem

## Slide 13: Defining the Timing Problem
Round Trip Delay (RTD) is being ignored
  Caused by computation delay and network delay.
Actual Receive Position =
Best
Average
Worst
Request Position
Expected Message Receive Position
Worst Case Receive Position Difference
IM
Actual Receive Position (ARP)

## Slide 14: Time Delays Will Cause Crashes
Intersection Manager
Request Line

## Slide 15: Accounting for Delays
A real intersection manager must also take into account delay in the system.
  Transmission Delay
  Computation Delay
  Summation: Round Trip Delay (RTD)
In existing implementations, delays will have to be modeled as additional Time Buffer around the vehicle:
36.885 milliseconds
(Source: our implementation)
123.791 milliseconds
(Source: our implementation)
150 milliseconds
(Source: our implementation)

## Slide 16: Real-life Computation and Network Delay
Chart: Round Trip Delay - Min, Avg, Max of 10 Tests
| 1 | 2 | 3 | 4
Max RTD | 39.408 | 65.568 | 83.848 | 135.836
Avg RTD | 30.8292 | 39.1102 | 48.7276 | 59.9947
Min RTD | 23.7 | 21.784 | 24 | 26.216

## Slide 17: How Large is the RTD Buffer
Using our real-life implementation, we measured how big a Safety Buffer considering RTD needed to be.
  .45m @ , 12.6km/h
    3x

## Slide 18: How Large is the RTD Buffer
Using our real-life implementation, we measured how big a Safety Buffer considering RTD needed to be.
    3.46x Original Vehicle Length

## Slide 19: Crossroads
Method #2 (Crossroads) - Our scheduling approach

## Slide 20: How We Solve RTD - Crossroads
We set the execution location according to Worst-Case Round-Trip Delay (WCRTD).
E
Best
Average
Worst
Request Position
Expected Message Execution Position = EP
IM
Actual Receive Position
Execution Position
Actuation Begins
Actuation Begins
Notes: Different animation, show 2 cars with different RTDs being fixed by execution position
Fix animation with expected location

## Slide 21: Crossroads Code
Vehicle Code:
1 SendRequest(){ // Sends request to enter the IM
send [, , LI, DI, LO, DO]; // Position, Velocity, Lane of // Entry, Direction of Entry, Lane of Exit, Direction of exit
Receive ;
Set = ; }
5 Interrupt(request line crossed){ // Received reply from IM
6 timeEapsed = 0; 7 SendRequest();
8 }
9 Interrupt(timeEapsed > timeout){ // Re-requests if no reply from IM
10 If( <= ){
11 = 0;
12 }
13 SendRequest(); }
Intersection Manager Code:
1 if(request received) {
AddVehicleToQueue();
= CalculateDesired;
s;
5 }
Notes: IM calculates the desired Time of Arrival, T oA, and the execution time, TE, (actuation position PE) based on WCRTD
Fix this slide

## Slide 22: Crossroads Eliminates Time Buffer
Unlike the VT-IM methodology, Crossroads does not require a Time Buffer
    ~ 3.5x Original Vehicle Length -> ~ 1.5x

## Slide 23: Related Work: Autonomous Intersection Management
Method #3 (AIM) - Avoids the RTD problem.

## Slide 24: AIM (Autonomous Intersection Management)
A tested and effective FCFS (First Come First-Served) policy
  Dresner and Stone propose and IM that:
    Vehicle requests to entire intersection at ToA and VoA
    IM simulates the trajectory of the vehicle
    Responds YES if the trajectory has no overlap with the reserved spots of other vehicles
    Responds NO otherwise.
Notes: Must state problem - RTD is ignored – the problem is RTD is ignored

## Slide 25: AIM is a query-based approach
Intersection Manager
Request Line
Enter
Exit
Request Time of Entry, (TOE) Velocity of Entry
Receive Accept
Vehicle Begins Actuation
of Proposed TOE
Notes: Explain timing problem and how it is solved

## Slide 26: Related Work: AIM
Vehicle Code:
1 SendRequest(){ // Sends request to enter the IM
send [, ]; // Position, Velocity, Lane of // Entry, Direction of Entry, Lane of Exit, Direction of exit
Receive ;
Set = ; }
5 Interrupt(request line crossed){ // Received reply from IM
6 timeEapsed = 0; 7 SendRequest();
8 }
9 Interrupt(timeEapsed > timeout){ // Re-requests if no reply from IM
10 If( <= ){
11 = 0;
12 }
13 SendRequest(); }
Intersection Manager Code:
1 if(request received) {
calculateIfSafe(, );
s;
5 }
Notes: Algorithm 3 needs to be more specific, use comments or descriptive name

## Slide 27: Related Work: AIM
Aim was tested virtually with 1 real and a number of simulated autonomous vehicles for the Darpa 2007 challenge
AIM was implemented in real life with Four 1/10 scale vehicles
  Vmax .5m/s, or at scale 18 km/h so they may have missed the problem
    √ Achieves a theoretical throughput of .5 vehicles/lane/s.
    √ Considers a Safety Buffer
    X Computation time is large
    X High communication overhead
    X Many re-requests
    X Cannot efficiently schedule vehicles
Notes: AIM communication overhead
AIM cannot re-schedule effeciently

## Slide 28: Scale Model Test Setup
Performed 10 intersection scenarios, 2 planned, 8 randomized – repeated each scenario 10 times
  = 1
  = .605 m
  = 3 m
  .568 m
  . 296 m
  3.0 m/s
1
1
1
1
Request
Line
Request
Line
Request
Line
Request
Line

## Slide 29: Results of Scale Models
Boundary Cases:
  SB – SafetyBuffer, TD – TransmitDistance, VL – Vehicle Length
Scenario 1
Scenario 10
Intersection Scenario #1 Heavy Traffic Load
Intersection Scenario #10 Light Traffic Load
Not to scale
Not to scale

## Slide 30: Crossroads Performs Better in Scale Tests
INTERSECTION SCENARIO NUMBER
Heavy
Traffic
Light
Traffic
Notes: Car arrival scenarios instead

## Slide 31: Simulation in Matlab, N=160

## Slide 32: Crossroads Performs Better in Simulation
.35 Traffic
Light
Max
Flow
.5 Round-
about
Light
Max
Flow
Notes: Figure out ideal that is possible
Mark interesting region
Mark traffic signal limits
Spend more time, add more slides

## Slide 33: Summary
An Intersection Manager (IM) must account for position uncertainty as a Safety Buffer
  Position uncertainty comes from sensors, actuators, etc.
An IM must account for timing problems as Time Buffer
  Computation Delay
  Network Delay
AIM solves timing problem with a yes/no approach.
Our technique (Crossroads) eliminates the Time Buffer
  It is replaced by timestamp-based execution
Crossroads maintains high schedulablility in addition to safety, thus increasing throughput
  1.62x Crossroads vs VT-IM and 1.36x Crossroads vs AIM on average
Notes: Missing main points
Needs work