## Slide 1: Software Coherence Management on Non-Coherent-Cache Multicores
Jian Cai, Aviral Shrivastava
Compiler Microarchitecture Lab
Arizona State University, USA

## Slide 2: Non-coherent-Cache Multicores
Coherence
  Mechanism by which cores get the latest copy of shared data
The overheads of cache-coherence increase with the number of cores
  Each core has to tell every other core about the data it is accessing
  Area and power of the coherence logic increases dramatically
Remove the cache coherence logic
  Intel 48-core Single-chip Cloud Computer
  Digital Signal Processors, e.g., the 8-core TI 6678

## Slide 3: Software Coherence Management
One way is to disable caches, and execute from main memory
Software Coherence Management
  identify the shared data
  fetch the latest copy of shared data before it is used –> by DMA instructions
  update it
  merge the updates back
Overhead of extra instructions
Performance will be dependent on:
  the memory consistency model
    how much we can reorder
  granularity of management
    how often we need to read/write
Notes: Timing of propagating writes is critical to implementation of coherence management

## Slide 4: Memory Consistency
Sequential consistency
  The order to each read and write to the memory must be maintained
  no out-of-order execution allowed
Relaxed consistency
  Memory accesses that can be reordered are within critical section, surrounded by acquire() and release()
  requires strict ordering only of acquire() and release()
  loads and stores can be reordered
Proc0 Proc1
acquire(lock)
write x
release(lock)
acquire (lock)
read x
write y
release (lock)
Notes: Timing of propagating writes is critical to implementation of coherence management

## Slide 5: Granularity of Management
Inter-core coherence is traditionally done in hardware at cache block granularity
  fine-grain management
Software cache coherence is typically implemented among processors
  page-level granularity
  coarse-grain management
Inter-core software cache-coherence must be:
  fine-grain
  less false sharing
  fast inter-core communication
Notes: IBM Cell processor is around 20 GFLOPS, while that of a conventional Intel Xeon processor reaches up to 600 GFLOPS

## Slide 6: State-of-the-Art: COMIC
P0
P1
Coherence Manager
acquire
release
acquire
time
write req.
write ack.
modified page
write req.
modified page
write ack.
modified
updated
modified
updated
twin
twin
modified
twin
modified
original
release
Page-level granularity
Requires a core to serve as coherence manager
Duplicates pages at acquire, and merges pages at release
Notes: When multiple writes try to write to different locations of the same page (false sharing), the coherence manager needs to create a twin page of the original page, and then creates a private copy of twin (not the original page) for each write request. When a requesting core finishes its modifications, it notifies the coherence manager, which then compares the modified private copy with twin , get the differences and apply the differences to the original page (not twin). The creation of the twin page and private copies for the writers are necessary, as otherwise the later modifications may overwrite the earlier modifications if all the writers writes to the original page directly. This whole process, especially the comparison of modified private copy of a writer to the twin page (which is done byte by byte), requires a lot of computation.

## Slide 7: Our approach
P0
P1
Main Memory
acquire
release
acquire
release
time
write req.
write ack.
writes + write notices
update original data
write req.
write ack. + write notice
update modified bytes
writes
read
create write notices
Byte-level granularity
No coherence manager
No duplicates and merges are required at acquire and release, respectively

## Slide 8: Write Notices
A record of a write (but not the value)
Write notices can be merged to improve performance
x = 5;
address: &x
size: sizeof(x)
a write:
write notice:
a[i]++;
address: &a[i]
size: sizeof(a[i])
write1:
write notice:
a[i+1]++;
address: &a[i+1]
size: sizeof(a[i+1])
write2:
write notice:
address: &a[i]
size: sizeof(a[i])*2
write notice:
merge
Notes: Make an example of merging write notice

## Slide 9: Performance Improvement
Chart: 
| Compress | Laplace | Lowpass | Wavelet | MMT | MV | MM | MT | Average
COMIC | 6.5486 | 9.8119 | 10.6159 | 3.4146 | 3.9372 | 4.1484 | 3.5364 | 3.1413 | 5.6443
Our Approach | 12.3635 | 19.6401 | 20.198 | 4.2282 | 11.3796 | 15.7355 | 5.5202 | 6.2523 | 11.9147

## Slide 10: Management Overhead Reduction
Chart: 
| Compress | Laplace | Lowpass | Wavelet | MMT | MV | MM | MT | Average
Actual Execution | 0.39416 | 0.64793 | 0.35557 | 0.62272 | 0.40203 | 0.66203 | 0.89584 | 0.94891 | 0.36541 | 0.91073 | 0.28038 | 0.85196 | 0.67195 | 0.94928 | 0.56594 | 0.88797 | 0.49141 | 0.81019
Coherence Management | 0.60584 | 0.35207 | 0.64443 | 0.37728 | 0.59797 | 0.33797 | 0.10416 | 0.051093 | 0.63459 | 0.089274 | 0.71962 | 0.14804 | 0.32805 | 0.050721 | 0.43406 | 0.11203 | 0.50859 | 0.18981
comic
our approach

## Slide 11: Summary and Future Work
Overhead of hardware coherence increases dramatically with the no. of cores
Software implemented coherence on Non-coherent-Cache architectures
  light hardware,
  but need to keep the software overhead of coherence management low
Presented
  Fine-grain coherence management in software
  No extra management core required
Ongoing work
  Integrate our approach into compiler
  Currently our work is provided as a run-time library
Future Work
  Software coherence management can be extended to SPM-based multicores
    SPM has 34% less area and consumes 40% less power than a cache of the same capacity
    Data transfers between main memory and SPM have to be managed by software

## Slide 12: Speaker: Aviral Shrivastava
Aviral Shrivastava is Associate Professor in the School of Computing, Informatics and Decision Systems Engineering at the Arizona State University, where he has established and heads the Compiler and Microarchitecture Labs (CML). He received his Ph.D. and Masters in Information and Computer Science from University of California, Irvine, and bachelors in Computer Science and Engineering from Indian Institute of Technology, Delhi. He is recipient of the 2011 NSF CAREER Award, and 2012 Outstanding Junior Researcher in the School of Computing, Informatics, and Decision Systems Engineering. His research focuses in three important directions, 1. Manycore architectures and compilers, 2. Programmable accelerators and compilers, and 3. Quantitative Resilience. His research is funded by DOE, NSF and several industries including Intel, nVIDIA, Microsoft, Raytheon Missile Systems, Samsung etc. He serves on organizing and program committees of several premier embedded system conferences, including ISLPED, CODES+ISSS, CASES and LCTES, and NSF and DOE review panels.

## Slide 13: If two cores modify the same data, then the updates will be overwritten
Yes, but that is what the programmer intended.
If the programmer wanted the updates to the same data in an order, or exclusively, they would have used locks or barriers
In parallel programming, the programmer has some responsibility in deciding the order to execution.
  locks provide exclusive access
  barriers provide ordered execution
If none of present
  implies that overwrites are acceptable

## Slide 14: Why does COMIC need triplicate pages?
modified
twin
original
Coherence Manager
Core 1
modified
compare
update
compare
Core 2
update

## Slide 15: Coherence vs. Consistency
Coherence is about memory accesses to the same address
  by different cores
  one core writes 5 to address A, and another one reads, it
  will it get the new value or the old
Consistency is about memory accesses to different addresses
  Core 1 writes to address X first, and address Y second
  Can these two writes to the main memory be reordered
  If they can be, then another core could read new value to Y, but old value of X
    sequential consistency says no reordering
    Relaxed consistency says, between acquire() and release(), all reordering is allowed.

## Slide 16: Previous Work: COMIC
P0
P1
Coherence Manager
acquire
release
acquire
release
time
write req.
write ack.
create a twin page, and a copy for P0
modified copy
create write notice, update original page
write req.
write ack. + write notice
Invalidate page
write to its private copy
page req.
updated page
read
Main Memory
create a twin page, and a copy for P1
Creating and merging duplicates is compute-intensive, but required when multiple writers try to modify different locations of the same page (false sharing), to prevent a writer from overwriting modifications of others, which may happen if writers write to the original page directly
Notes: Write notices are needed to tell processors if pages they need to access has been updated

## Slide 17: Advantages of Our Approach
P0
P1
Main Memory
acquire
release
acquire
time
write req.
write ack.
modified bytes
write req.
modified bytes
write ack.
modified
updated
modified
updated
original
False sharing happens at smallest resource block (such as a cache line or a page) which depends on the granularity of coherence management
Our byte-level approach eliminates false sharing, and thus avoid creating duplicates and merging them at acquire and release operations as in COMIC
release
Notes: False sharing happens at smallest resource block (such as a cache line or a page) which depends on the granularity of coherence management. Since our approach manages coherence at bytes, it guarantees no two writes will happen in the same resource block (otherwise it is a true sharing, which should be taken care by programmers). This property eliminates false sharing and thus the compute-intensive process of creating and merging duplicates as in COMIC.