## Slide 1: RAMP: Resource-Aware Mapping for CGRAs
Shail Dave, Mahesh Balasubramanian, Aviral Shrivastava
Compiler Microarchitecture Lab,
Arizona State University

## Slide 2: Coarse Grained Reconfigurable Array (CGRA)
Quick Facts
  CGRAs can achieve power-efficiency of several 10s of GOps/Sec per Watt!
    ADRES CGRA, upto 60 GOps/sec per Watt [IMEC, HiPEAC 2008]
    HyCUBE, about 63 MIPS/mW [Karunaratne M. et al., DAC 2017]
  Popular in Embedded Systems and Multimedia [Samsung SRP processor]
An array of Processing Elements (PEs); each PE has ALU-like functional unit that works on an operation at every cycle.
Array configurations vary in terms of –
  Array Size ► Reg. File Architectures
  Functional Units ► Interconnect Network

## Slide 3: Mapping Loops on CGRAs
Iterative Modulo Scheduling
  Each loop iteration is executed at II cycles [Bob Rau, MICRO 1994]
II = 2
a
b
c
1
d
1
2
a
i=0
b
c
a
d
i=1
time
1
2
3
B = 0;
for(i=0; i<1000; i++)
{
A = B - 4;
B = A + L;
C = A * 3
D = C + 7;
}
a:
b:
c:
d:
Sample Loop
DDG
Modulo Schedule
1
2
1
1x2 CGRA
4 operations to map on 2 PEs => minimum initiation interval (MII) is 2 cycles.
Software Pipelining
  Operations from 2 different iterations execute simultaneously
The Code Generation Battle
  The performance (loop execution time) critically depends on the mapping obtained by compiler
  Mapping problem boils down to routing problem
    In a temporal-spatial solution set, if all the dependent operations are placed on those PEs which can directly communicate the resultant values at time being, mapping (placement) is trivial.
    Routing is needed when the dependent operations can be scheduled at a distant time, or operations cannot be mapped due to resource constraints.

## Slide 4
What are the Various
Routing Strategies

## Slide 5: Routing Data Dependency via PEs
1
2
DDG
Modulo Schedule (II = 3)
1
3
1
2
1x2 CGRA
time
1
2
b
3
c
a
ar
To achieve a mapping,
Need to route a → d
Insert a routing operation Place it on an empty PE slot
(EMS[1], EPIMap[2])
►
P&R
[1] H. Park et al., Edge-centric modulo scheduling for coarse-grained reconfigurable architectures. In PACT, 2008.
[2] M. Hamzeh et al., Epimap: using epimorphism to map applications on cgras. In DAC, 2012.
c
a
b
d
4
d
arr
a
Notes: 1.5-2

## Slide 6: Routing Data Dependency via Registers
[3] L. Chen et al., Graph minor approach for application mapping on cgras. ACM TRETS, 2014.
[4] M. Hamzeh et al., Regimap: Register-aware application mapping on cgras. In DAC, 2013.
DDG
Modulo Schedule (II = 2)
1
1
2
2
c
a
b
d
time
1
2
b
3
c
a
P&R
4
d
a
a0
b
a0
a0
a1
a0
a1
1
R1
2
R1
R2
R2

## Slide 7: Routing Data Dependency via Memory
[5] S. Yin et al., Memory-aware loop mapping on coarse-grained reconfigurable architectures. IEEE TVLSI, 2016.
1
2
DDG
Modulo Schedule (II = 3)
1
3
1
2
1x2 CGRA
time
1
2
b
3
c
a
Sa
P&R
c
a
b
d
4
d
La
a

## Slide 8: Analyzing Impact of Ad-hoc Routing Strategies
For the top performance-critical loops from 8 MiBench benchmarks, previous techniques failed to obtain mappings for almost all loops, when highly constrained by the resources.
The mapping quality obtained is far from the best possible mapping (II = MII), even when the target CGRA has higher resources (including manual attempts to achieve better mapping).

## Slide 9: CGRA Code Generation Maze

## Slide 10
Valid mappings (with
Nearly optimal Quality)

## Slide 11: RAMP: Resource-Aware Mapping
DDG
a
e
b
c
d
2
1
time
b
c
d
e
i
a
a
t
t+1
t+3
t+2
t+4
1
2
R1
R1
1x2 CGRA
Mapping Attempt (II = 4)
Initially Route All Dependencies
Through Direct PE Communication
Need to Route
?

## Slide 12: RAMP: Resource-Aware Mapping
DDG
a
e
b
c
d
2
time
b
c
d
e
i
a
a
ei-1
ei-1
ei-1
ei
1
ai
ai
ai
ai
ai+1
ei
t
t+1
t+3
t+2
t+4
1
2
R1
R1
1x2 CGRA
Mapping Attempt (II = 4)
Initially Route All Dependencies
Through Direct PE Communication
And via Registers

## Slide 13: RAMP: Resource-Aware Mapping
DDG
a
e
b
c
d
2
time
b
c
d
i-1
e
i
a
a
ei-1
ei-1
ei-1
ei
1
ai
ai
ai
ai
ai+1
ei
t
t+1
t+3
t+2
t+4
1
2
R1
R1
1x2 CGRA
Mapping Attempt (II = 4)
b → e might be routed by
Spilling to memory
Distributed Registers
PEs
br
2
1
e
Modified
DDG
a
b
c
d
br

## Slide 14: RAMP: Resource-Aware Mapping
time
b
c
d
i-1
e
i
a
II = 4
a
ei-1
ei-1
ei-1
ei
ld
br
Sd
Sd
ai
ai
ai
ai
ai+1
ei
t
t+1
t+3
t+2
t+4
1
2
R1
R1
1x2 CGRA
Mapping Attempt (II = 4)
di → ci-2 might be routed by
Spilling to memory
Distributed Registers
PEs
Mapping is Combination of:
- Routing via PEs
- Routing via Registers
- Spilling to Memory
DDG
a
e
b
c
d
2
1
br
Modified
DDG
a
e
b
c
d
1
br
Ld
Sd

## Slide 15: Selecting a Routing Alternative
Failure Analysis
  Dependent operations are scheduled at distant time; managing the data with large lifetime in registers is not possible
    Route by PEs, Spill to memory/distributed RFs
  Dependent operation is a live value, cannot be managed in the register.
    Manage live value in the memory
  Dependent operations are scheduled at the consequent time; routing is not possible due to limited interconnect/unavailability of free PEs
    Re-compute, Route by a PE, Re-schedule
Graph Modification and Rescheduling

## Slide 16: RAMP Enables Spilling to Distributed RFs
Based on the distant schedule time of dependent operations, RAMP determines number of distributed registers required.
  Before the source operation (e) of the next iteration (ei+1) over-writes the value, insert a RF-read operation err.
  If the destination operation (ai) is scheduled far than ewr, insert a RF-write operation.
  P&R should ensure that operations err and ewr are mapped onto the PEs that don’t share RF.
time
t
t+1
t+3
c
d
a
b
i
t+2
t+4
ei-1
ei
e
f
ei-1
ei-1
ei-1
t+5
h
g
f
err
ei-2
ei-2
ei-2
ei-1
ei-1
ei-1
erw
a
ei
II = 5
1
2
R1
R1
e
f
d
g
b
c
a
2
h

## Slide 17: Experimental Setup
Benchmarks
  MiBench suite [Guthaus et al., IEEE WWC 2001] (top performance critical loops)
Compilation
  CCF: CGRA Compilation Framework (LLVM 4.0 [Lattner et al., CGO 2004] as foundation)
  Optimization level 3
Simulation
  Cycle-Accurate CCF-Simulator (based on gem5 [Binkert et al., SIGARCH Comp. Arch. News 2001])
    CGRA modeled as a separate core coupled with ARM Cortex-like processor core
    PEs connected in a 2D torus, perform fixed-point computations
    CGRA accesses 4 kB data memory and 4 kB instruction memory
Techniques Evaluated
  Register-aware mapping - REGIMap [Hamzeh et al., DAC 2012]
  Memory-aware mapping - MEMMap [Yin et al., IEEE TVLSI 2016]
  Resource-aware mapping - RAMP

## Slide 18: RAMP Improves CGRA’s Acceleration Capability by 2.13×
With systematic resource exploration, RAMP achieved better mapping, outperforming state-of-the-art.
  It spills to memory and/or exploits the distributed registers, when the resources are limited.
  Generated mapping features combination of various routing strategies to route different data dependencies.
Scaled well with the availability of different architectural resources.
  RAMP adapts to the needs of the application, flexibly exploring resources via the various routing strategies.
Total Loops Mapped
Speedup
0
5
10
0
20
10
4
8
12
Architecture Configuration
Resources
RAMP
REGIMap
MEMMap
Increase in
RAMP accelerated loops by 23× as compared to sequential execution, and by 2.13× over REGIMap, and by 3.39× over MEMMap.
Architectural

## Slide 19: RAMP Achieves Nearly Best Possible Mapping
Since RAMP systematically explored resources, it spilled data to memory only after using the available registers, minimizing routing operations
  E.g. jpeg encoding
New routing strategy of utilizing distributed registers yielded better mappings for susan, adpcm etc.
Mapping Quality for Config#7 (4x4CGRA_LRF4)
To map unmapped operations, RAMP systematically explored the various routing strategies, instead of implicitly performing P&R in an ad-hoc manner.
  RAMP was able to achieve better mapping with inserting less routing/memory operations.
With less operations to be mapped, RAMP observed same computational complexity as other clique-based mapping heuristics e.g. REGIMap or MEMMap.
Chart: Benchmarks
| sha | bitcount | susan_smooth | adpcm_enc | gsm_short | gsm_long | jpeg_enc | adpcm_dec | geomean
MEMMap | 0.33333 | 1 | 0.16667 | 1 | 0.18293 | 0 | 0.25 | 0.33333 | 0.36401
REGIMap | 0.42857 | 1 | 0.33333 | 1 | 0.24194 | 0.28571 | 0.4 | 0.54545 | 0.46416
RAMP | 1 | 1 | 1 | 1 | 0.83333 | 0.83333 | 0.66667 | 1 | 0.90822
gsm_ short
gsm_ long
susan_ smooth
geo mean
jpeg _enc
adpcm _enc
sha
bitcount
adpcm _dec
Higher the Better
0.91

## Slide 20: Summary
The goodness of the obtained mapping is critically dependent on how efficiently the compiler can route the data dependencies.
Existing mapping techniques are unable to make good use of the routing resources. They first schedule the DDG and then attempt the P&R; routing is internal to P&R and is carried out in an ad-hoc manner. Hence,
  Operations may not be mapped due to resource constraints, or
  Obtain poor code quality.
RAMP models various routing strategies explicitly. It systematically and flexibly explores available architectural resources for routing the data dependencies.
  Enables effective utilization of distributed registers and spilling to memory.
  Failure analysis allows to systematically choose the routing alternatives to map a data dependency.
  With comprehensive problem formulation, RAMP exploits heterogeneous architectural resources.
RAMP accelerated the top performance-critical loops of MiBench by 23× over a sequential execution, and by 2.13× over state-of-the-art techniques.

## Slide 21
Thank you !

## Slide 22: Additional Slides
Inefficiencies of the Mapping Heuristics with Ad-hoc Routing Strategies

## Slide 23: Routing Data Dependency via PEs
e
a
d
c
1
2
DDG
Schedule (II = 3)
1
3
1
2
1x2 CGRA
time
1
2
d
a
3
e
c
ar
To achieve a mapping,
Need to route a → e
Insert a routing operation Place it on an empty PE slot
(EMS[1], EPIMap[2])
►
P&R
e
a
b
d
c
DDG
1
3
1
2
2
time
1
2
d
a
3
e
c
P&R
b
ar
?
Since ar is not rescheduled,
cannot route a → e
time
1
2
d
a
3
e
c
P&R
b
ar
Rescheduling (+ path-sharing) can enable a mapping.
►
[1] H. Park et al., Edge-centric modulo scheduling for coarse-grained reconfigurable architectures. In PACT, 2008.
[2] M. Hamzeh et al., Epimap: using epimorphism to map applications on cgras. In DAC, 2012.

## Slide 24: Routing Data Dependency via Registers
GraphMinor[3] and REGIMap[4] allow routing dependency via registers.
  To route the data dependency via register file of a PE, both the dependent operations (e and a) must be placed on the same PE.
  Typically, for CGRA with local/distributed registers, target PE should have enough registers available to route the data dependency.
    E.g., dependency e → a is routed only if the PE1 have 2 registers.
Challenge?
  Routing dependency by efficiently utilizing distributed registers of different PEs.
time
t
t+1
t+3
c
d
a
b
i
t+2
t+4
ei-1
ei
e
f
ei-1
ei-1
ei-1
t+5
e
f
d
g
b
c
a
2
h
h
g
1
2
R1
R1
?
ei-1
a
i+1
[3] L. Chen et al., Graph minor approach for application mapping on cgras. ACM TRETS, 2014.
[4] M. Hamzeh et al., Regimap: Register-aware application mapping on cgras. In DAC, 2013.

## Slide 25: Routing Data Dependency via Memory
MEMMap [5] statically determines to manage values with large lifetime in memory, avoiding the need of re-scheduling DDG
Challenges ?
  Routing data dependency via memory (spilling) requires additional memory operations, and without re-scheduling the DDG, they might not be mapped!
  With sufficient registers and PEs, such dependencies might be better managed via registers.
  For a resource-constrained CGRA target, the variable value has to be spilled, even though its lifetime is less than the pre-set threshold.
[5] S. Yin et al., Memory-aware loop mapping on coarse-grained reconfigurable architectures. IEEE TVLSI, 2016.
b
e
a
f
c
d
g
1
time
1
2
4
3
5
6
c
b
d
a
i
e
f
g
lb
la
?
sa
sb
1
2
R1
R1

## Slide 26: Additional Slides
A High-Level Overview of RAMP

## Slide 27: RAMP: Resource-Aware Mapping
Partition mapping in 3 sub problems:
  Systematically explore routing strategies
  Re-scheduling and
  Place and Route
Spill to Memory
Routing via PEs
and/or Registers
Spill to other distributed RFs
Re- Compute
Route via PE
Change Schedule Time
Routing
Strategy
Load Read-Only Data From Memory
1
2
3
Re-Schedule
Place & Route
Failure Analysis
For selected routing strategy, DDG is modified and re-scheduled.
  Additional constraints: for spilling data to memory, a store must occur before a load!
Check whether the opted strategy(ies) routed the targeted data dependency.
  For multiple strategies being successful, choose the one which maps more operations, and requires minimum PEs to map.
    Take new modified and mapped graph, and try mapping remaining dependencies at targeted II.
  If no strategy can route a dependency, need to increase II by 1, and start over.
For example, we can choose to first map the DDG with routing via registers. Then, for any unmapped data dependency, explore different routing options.