## Slide 1: nZDC: A compiler technique for near-Zero silent Data Corruption
Moslem Didehban, Aviral Shrivastava
Arizona State University

## Slide 2: Need to detect SDCs by software techniques
Transient faults/Soft errors as a major threat for reliability
Silent data corruption (SDC) as the most difficult errors to detect
  Usually not generating any symptom
  Not detectable by simple hardware/software detectors
Full replication
  Software-level
    Flexible
  Hardware-level
    Considerable hardware modification is necessarily!
    Not possible in resource-constrained embedded systems
Check the results for error detection
Notes: Ever-increasing usage of digital devices in todays life, has made reliability as one of the most important design concerns.
Transient faults or soft errors have been considered as the major threat for modern microprocessor reliability.
Some soft errors cause abnormality in program execution and are easily detectable by operating systems. However, some errors go unnoticeable and lead to an incorrect output. These errors are called Silent Data Corruptions or SDC.
Full duplication is one way to protect the computation from soft errors.
If full duplication takes place in hardware-level it will be very expensive – because a fully duplicated processor needs as more than twice transistors as a normal processor
Software-level full duplication, however, can provide full error coverage without any additional hardware cost.

## Slide 3: Software-level full duplication is not as easy as it sounds!
Process-level duplication
  I/O can not get duplicated
  Checking before library calls
    How to check? – inter-process communication is needed
    What to check? – arguments are usually pointers
  Needs operating system modifications
Assembly-level Instruction replication
  Provide fine details of the actual execution
  Compatible with compiler optimizations
  SWIFT (SoftWare Implemented Fault Tolerance)
Notes: SWIFT has more than 500 citatins
Works after SWIFT, admit to near perfect fault coverage of SWFT and try to improve its performance overhead

## Slide 4: SWIFT (SoftWare Implemented Fault Tolerance)
cmp x1, x1*
b.ne error
load x2, [x1]
mov x2*, x2
mov x1, #0x04
mov x1*, #0x04
add x2, x2, #0x10
add x2*, x2*, #0x10
and x1, x2, #0x10
and x1*, x2*, #0x10
cmp x2, x2*
b.ne error
cmp x1, x1*
b.ne error
store x2, [x1]
mov
mov
store
add
add
and
and
= Vulnerable
= Protected
load
Checking Value
Load value duplication
Checking Address
Checking Value
mov x1, #0x04
load x2, [x1]
add x2, x2, #0x10
and x1, x2, #0x10
store x2, [x1]
Unreliable Code
  Duplicate computational instructions
  Check before memory and compare instructions
Notes: In this slide, I show the state-of-the-art instruction duplication technique, which is called SWIFT. Leveraging this fact that the memory subsystem can be protected by ECC efficiently, SWIFT duplicates all instructions and check for the errors before memory and compare instructions.
SWIFT transformation divides the instructions inside a program into two groups: 1) duplicable or protected, and, non-duplicable or unprotected. So, the question is how big are these unprotected instructions.

## Slide 5: SWIFT leaves more than 40% of the instructions as unprotected
Source: “MiBench: A free, commercially representative embedded benchmark suite.” The University of Michigan.
Notes: This figure show the dynamic instruction distribution for Mibench and speech benchmarks program.

## Slide 6: SWIFT Sphere of protection
Protected by ECC
  Data and Instruction caches
Not Protected
  Only unduplicated instructions using these resources (loads, Stores and branches)
Partially Protected
  Unprotected during the execution of unduplicated instructions (loads, Stores, branches and Compares)
Completely Protected by SWIFT
  Always duplicated instructions (logical and computational instructions)
L1 Instruction Cache
L1 Data Cache
Fetch
Issue
Decode
Write Back
Register
File
S
L
F1
F2
M
B
I1
I0
Load
Multi-Cycle ALU
Branch
Integer ALU
Integer ALU
Load-Store Unit
Store Buffer
Store
Protected by ECC
Unprotected
Partially Protected
Completely Protected
NEON/FPU
NEON/FPU

## Slide 7: nZDC: Compiler transformations for complete protection
Goal
  Protect the execution of all instructions in all hardware components
Duplicate all instructions
  Logical and Computational Instructions
    Already duplicated by SWIFT
  Memory read instructions
  Memory write instructions!
    Checking load instructions as duplication
    for Stores
  Compare instructions
    Get duplicated by nZDC CFC
  Branch instructions!
    Direction is checked as well as the
    target address
L1 Instruction Cache
L1 Data Cache
Fetch
Issue
Decode
Write Back
Register
File
S
L
F1
F2
M
B
I1
I0
Load
Multi-Cycle ALU
Branch
Integer ALU
Integer ALU
Load-Store Unit
Store Buffer
Store
Protected by ECC
Unprotected
Partially Protected
Completely Protected
NEON/FPU
NEON/FPU

## Slide 8: nZDC data flow transformation
mov x1, #0x04
load x2, [x1]
add x2, x2, #0x10
and x1, x2, #0x10
store x2, [x1]
Unreliable Code
mov x1, #0x04
mov x1*, #0x04
add x2, x2, #0x10
add x2*, x2*, #0x10
and x1, x2, #0x10
and x1*, x2*, #0x10
store x2, [x1]
load x2, [x1*]
cmp x2, x2*
b.ne error
load x2, [x1]
load x2*, [x1*]
Duplicate all data-flow instructions
Check for correct execution after stores
Load back the written value from the memory and check against the stored value
Notes: Main idea: Duplicates all data-flow instructions and check for the correct execution after stores by loading back from the memory and comparing the loaded value against the written value

## Slide 9: Check memory write instructions
store x2, [x1]
load x2, [x1*]
cmp x2, x2*
b.ne error
Duplicable
computations
++ “store” is protected
++ optimal number of checks
nZDC
cmp x1, x1*
b.ne error
cmp x2, x2*
b.ne error
store x2, [x1]
Duplicable
computations
-- RF vulnerable intervals
-- “store” is unprotected
SWIFT
store x2, [x1]
cmp x1, x1*
b.ne error
cmp x2, x2*
b.ne error
Duplicable
computations
++ Eliminate RF vulnerable intervals
-- “store” is unprotected
Check after store
store x2, [x1]
load x2*, [x1*]
cmp x1, x1*
b.ne error
cmp x2, x2*
b.ne error
Duplicable
computations
++ address part is protected
-- data part is vulnerable
Checking load

## Slide 10: nZDC detects all SDC
0.0
nZDC and SWIFT are implemented as late backend passes in LLVM 3.7
More than 70K faults are injected in an ARM-cortex A53 like processor in Gem5

## Slide 11: nZDC Control flow mechanism is very effective
Faults are injected on Branch and compare instructions
Chart: Control flow instruction fault distribution
| ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | ORG | SWIFT | ZDC | SHA | CRC | Qsort | Rijndael | FFT | Dijkstra | Basicmath | Stringsearch | Bitcount | Blowfish | AVG
Masked | 48.85 | 45.1777 | 8.1686 | 94.1292 | 87.1429 | 5.7587 | 29.6 | 35.6568 | 9.1703 | 49.8588 | 65.1042 | 67.5676 | 48.6441 | 65.1042 | 43.7396 | 65.764 | 58.982 | 75.3799 | 45.7487 | 59.8913 | 41.3223 | 40.376 | 56.9665 | 65.9813 | 10.8309 | 21.2636 | 12.9231 | 48 | 56.0976 | 10.1523 | 48.1802 | 55.1387 | 34.0164
Detected/SegFault | 46.9 | 51.5921 | 91.5193 | 5.5773 | 10 | 94.1499 | 17.8667 | 5.0938 | 90.393 | 37.7119 | 31.7708 | 32.4324 | 44.7458 | 31.7708 | 55.9265 | 30.5609 | 38.6228 | 24.3161 | 16.93 | 8.4783 | 58.0165 | 54.8791 | 37.6249 | 32.7103 | 36.6963 | 12.2283 | 87.0769 | 47 | 38.0488 | 89.3401 | 33.8868 | 26.5231 | 65.5881
SDC | 4.25 | 3.2303 | 0.31217 | 0.29354 | 2.8571 | 0.091408 | 52.5333 | 59.2493 | 0.43668 | 12.4294 | 3.125 | 0 | 6.6102 | 3.125 | 0.33389 | 3.675 | 2.3952 | 0.30395 | 37.3213 | 31.6304 | 0.66116 | 4.7449 | 5.4086 | 1.3084 | 52.4728 | 66.5082 | 0 | 5 | 5.8537 | 0.50761 | 17.933 | 18.3383 | 0.39553
18%
0.4%
nZDC-protected programs execute faster than SWIFT-protected ones

## Slide 12: Summary
  Soft error problem can be solved by software-only fault tolerant techniques
  Full instruction duplication should solve the problem
    Full duplication is not effective in some cases…
      Memory write operations
      Branches
      FLAG register
    However, the correct execution should be checked
  Branch direction checking is important
  nZDC provides complete processor-level protection in software, at competitive overhead as hardware techniques