## Slide 1: InCheck: An In-application Recovery Scheme for Soft Errors
Moslem Didehban
Sai Ram Dheeraj Lokam
Aviral Shrivastava

## Slide 2: Silent Data Corruption in processor-wide Fault Injection
ARM Cortex
A 53
Recognizable Change
in program behaviour
Silent Data Corruption - SDC
Un-Recognizable Change
in program behaviour
No Change
in program behaviour
Segmentation Fault
Program Abort
Masked
Recovered (Not applicable to unprotected programs)
72,000 Random Faults
Processor components subjected to FI
  Register File
  Load Store Queue
  Pipeline Registers
  Functional Units
Chart: Number of SDCs
| stringsearch | qsort | bitcount | crc32 | sha | fft | basicmath | rijndael | blowfish | TOTAL
Original | 92.8 | 663.4 | 712 | 1598.8 | 1274.6 | 851.4 | 718.8 | 1205.4 | 928 | 8045.2
InCheck | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Notes: ITRS roadmap for 2015 lists Muon-induced soft-errors as a major reliability challenge in both near term and long term microprocessor designs.

## Slide 3: Goal of InCheck:
Implementing a software level protection technique which,
  guarantees “Zero” Output Corruption
  provides “Safe” recovery from detected soft-errors

## Slide 4: Software techniques to detect SDCs
Flexibility
  They can optimized based on the workload characteristics without having to change the hardware
Coverage
  There are software techniques that can provide very good SDC coverage.
  Eg. nZDC (DAC 2016)
Notes: Safety critical applications are mixed critical

## Slide 5: SWIFT-R Transformation
majority_voting (x1, x1*, x1**)
load x2, [x1]
mov x2*, x2
mov x2**,x2
mov x1, #0x04
mov x1*, #0x04
mov x1**, #0x04
add x2, x2, #0x10
add x2*, x2*, #0x10
add x2**, x2**, #0x10
and x1, x2, #0x10
and x1*, x2*, #0x10
and x1**, x2**, #0x10
majority_voting (x2, x2*, x2**)
majority_voting(x1, x1*, x1**)
store x2, [x1]
majority_voting (R, R*, R**)
cmp R, R*
b.ne recover from R**
cmp R,R**
b.ne recover from R*
cmp R*,R**
b.ne recover from R
SWIFT-R
mov x1, #0x04
load x2, [x1]
add x2, x2, #0x10
and x1, x2, #0x10
store x2, [x1]
Original Code

## Slide 6: Original vs SWIFT-R SDC Distribution
Chart: Number of SDCs
| stringsearch | qsort | bitcount | crc32 | sha | fft | basicmath | rijndael | blowfish | TOTAL
Original | 92.8 | 663.4 | 712 | 1598.8 | 1274.6 | 851.4 | 718.8 | 1205.4 | 928 | 8045.2
SWIFT-R | 30.2 | 588.4 | 173.2 | 227.2 | 246.6 | 155.6 | 156.4 | 112.8 | 150.8 | 1841.2
InCheck | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 7: Pitfalls of SWIFT-R
Un-safe Recovery
cmp x1, x1* b.ne recover from x1** cmp x1, x1**
b.ne recover from x1*
cmp x1*, x1**
b.ne recover from x1
load x2, [x1]
mov x2*, x2
mov x2**,x2
load x2, [x1]
LET happens on x1 after compare
Majority
Voting
x1 recovered at next majority voting

## Slide 8: Pitfalls of SWIFT-R
store x2, [x1]
majority_voting (x2, x2*, x2**)
majority_voting(x1, x1*, x1**)
store x2, [x1]
Majority
Voting in performance critical path
++ Vulnerability ++ Execution time
majority_voting (R, R*, R**)
cmp R, R*
b.ne recover from R**
cmp R,R**
b.ne recover from R*
cmp R*,R**
b.ne recover from R
Notes: Reserved 60% of regs. Talk about register spilling.

## Slide 9: SWIFT-R vs InCheck SDC Distribution
Chart: Number of SDCs from processor wide fault injection
| stringsearch | qsort | bitcount | crc32 | sha | fft | basicmath | rijndael | blowfish | TOTAL
Original | 92.8 | 663.4 | 712 | 1598.8 | 1274.6 | 851.4 | 718.8 | 1205.4 | 928 | 8045.2
SWIFT-R | 30.2 | 588.4 | 173.2 | 227.2 | 246.6 | 155.6 | 156.4 | 112.8 | 150.8 | 1841.2
InCheck | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0
0
0
0
0
0
0
0
0
0

## Slide 10: InCheck Framework
Verified Register Preservation
Memory Checkpointing
Store
Error Detected?
Is recovery Safe?
Unrecoverable
Error
NO
YES
Memory Restoration
Registers Restoration
Rollback to .BB
Recovery
Diagnosis
Redundant
Computations
YES
.BB
(*Ensures no Latent Error)

## Slide 11: Performance evaluation:
Chart: Execution time normalized to Original Program
| stringsearch | qsort | bitcount | crc32 | sha | fft | basicmath | rijndael | blowfish | AVERAGE
Original | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SWIFT-R | 3.7323 | 3.1861 | 3.8073 | 3.2999 | 5.293 | 3.8573 | 3.4944 | 12.7342 | 2.5955 | 4.6667
InCheck | 2.5611 | 3.9289 | 2.3832 | 2.3832 | 2.5232 | 3.1194 | 3.4564 | 3.2749 | 3.1287 | 2.9732
nZDC+InCheck programs run 36% faster than their SWIFT-R counterparts

## Slide 12: Breakdown of Recoverable & UnRecoverable Errors in InCheck
Chart: % of Errors Detected Errors
| stringsearch | qsort | bitcount | crc32 | sha | fft | basicmath | rijndael | blowfish | AVERAGE
Recovered | 0.9 | 0.9236 | 0.9817 | 0.9743 | 0.958 | 0.965 | 0.9637 | 0.892 | 0.911 | 0.94103
Detected/UnRecoverable | 0.1 | 0.0764 | 0.0183 | 0.0257 | 0.042 | 0.035 | 0.0363 | 0.108 | 0.089 | 0.058967

## Slide 13: Thank you!

## Slide 14: Back up

## Slide 15: Statistical Fault Injection
N – Initial Population Size
p – estimated probability of faults resulting in a failure (standard error)
e – margin of error
t – confidence level. Probability that the exact value is actually within the error interval (computed w.r.t Normal distribution)
*Leveugle, Régis, et al. "Statistical fault injection: quantified error and confidence." 2009 Design, Automation & Test in Europe Conference & Exhibition. IEEE, 2009.

## Slide 16: SWIFT vs SWIFT-R
Chart: Number of SDCs
| stringsearch | bitcount | sha | qsort | crc32 | fft | basicmath | rijndael | blowfish | Total
ORG | 48 | 196 | 746 | 178 | 106 | 144 | 174 | 256 | 174 | 2022
SWIFT | 6 | 4 | 2 | 7 | 3 | 1 | 14 | 1 | 6 | 44
SWIFT-R | 8 | 58.6 | 57 | 373 | 97.8 | 14.4 | 41.6 | 11.2 | 82 | 743.6