## Slide 1: NEMESIS: A Software Approach for Computing in Presence of Soft Errors
Moslem Didehban, Aviral Shrivastava, Sai Ram Dheeraj Lokam

## Slide 2: Reliability is important!
Notes: Todays computer based systems are virtually everywhere,
inside our body … wearables and
Many of this applications are either safety or mission critical
For example, CPS systems like autonomous cars and drones, are clearely safety critical … and their failure come with severe consequences…

## Slide 3: Soft error protection is required
Soft errors: Historically, a problem for high-altitude applications
ITRS 2015 predicts soon even ground-level applications will be at risk.
Failure rate is expected to increase:
  More components  more failures
Solution: Redundancy
  Hardware-level solutions
    ARM Cortex-R Dual lockstep processor
  Software-level solutions
    Time redundancy (Flexible)
Notes: Transient faults/Soft errors a major thread for reliability
  Die size grows by ~14% to satisfy mores low
  Threshold voltage decreases
  Hundred times more frequent than hard errors
Sources of soft errors
  Cosmic rays and alpha particles
  Noise in power supply
  Electromagnetic interference
  Temperature, pressure, voltage, vibrations
“The nation depends on fragile software”
  Information Technology Research: Investing in Our Future, 1999

## Slide 4: Software-level error resilience scheme
Instruction-level soft error tolerant schemes
Error Detection
Examples: EDDI[2002], SWIFT[2005], Shoestring[2010], DRIFT[2013], SIMD-Based Soft Error Detection [16], IPAS [2016], nZDC [2016]
Majority-voting
Examples: SWIFTR[2007], selective-SWIFTR[2013], ELZAR [2016]

## Slide 5: A Closer Look into SWIFR
Majority-voter(val, val*, val**)
Majority-voter(adr, adr*, adr**)
store val[addr]
movl -4(%rbp), %eax
cmpl -8(%rbp), %eax
jne .L2
movl -4(%rbp), %eax
cmpl -12(%rbp), %eax
jne .L2
movl -8(%rbp), %eax
cmpl -12(%rbp), %eax
je .L6
.L2:
movl -4(%rbp), %eax
cmpl -8(%rbp), %eax
jne .L4
movl -4(%rbp), %eax
movl %eax, -12(%rbp)
jmp .L6
.L4:
movl -4(%rbp), %eax
cmpl -12(%rbp), %eax
jne .L5
movl -4(%rbp), %eax
movl %eax, -8(%rbp)
jmp .L6
.L5:
movl -8(%rbp), %eax
cmpl -12(%rbp), %eax
jne .L6
movl -12(%rbp), %eax
movl %eax, -4(%rbp)
.L6:
if ((adr != adr*) || (addr != adr **) || (adr * != adr **)){
if (adr == adr *) // addr ** is faulty
adr ** = adr;
else if (adr * == adr **) // addr is faulty
adr = adr *;
else if (adr == adr **) // addr * is faulty
adr * = adr;
}
val*, addr*
val, addr
Val**, addr**
Redundant computations

## Slide 6: Limitations of SWIFTR
Almost half of instructions (memory and control flow) are unprotected
Register file vulnerability introduced by frequent and long voting operations
  Majority voting operations should take place before all memory and compare operations
Chart: 
| stringsearch | bitcount | sha | qsort | CRC | FFT | dijkstra | basicmath | rindeal | blowfish | adpc-c | adpc-d | avg
Computational | 0.2723 | 0.80657 | 0.639 | 0.51052 | 0.54545 | 0.6162 | 0.4314 | 0.65291 | 0.63931 | 0.41967 | 0.60892 | 0.62499 | 0.56394
Mem and Compare | 0.52595 | 0.15208 | 0.30713 | 0.34083 | 0.27273 | 0.2975 | 0.3674 | 0.23268 | 0.34986 | 0.27345 | 0.35339 | 0.32288 | 0.31632
Branch | 0.20175 | 0.041356 | 0.05387 | 0.14865 | 0.18182 | 0.086298 | 0.2012 | 0.11441 | 0.010822 | 0.30688 | 0.037683 | 0.052131 | 0.11974
~45%

## Slide 7: Experimental results
Chart: Number of SDCs
| stringsearch | bitcount | sha | qsort | CRC | FFT | dijkstra | basicmath | rindeal | blowfish | adpcm-c | adpcm-d | Total
Original | 2516 | 25281 | 41781 | 21874 | 80711 | 14421 | 232 | 9783 | 28348 | 27344 | 27430 | 35095 | 237059
SWIFTR | 508 | 7545 | 14306 | 15150 | 15996 | 4283 | 95 | 7442 | 24263 | 12275 | 14161 | 13994 | 120664
Nemesis | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
(~5%)
(~2.4%)
ARM Cortex
A 53
Recognizable Change
in program behaviour
Silent Data Corruption
Wrong Output
No Change
in program behaviour
Segmentation Fault
Program Abort
Masked
Recovered
Notes: 10 million micro-architectural level random fault injection experiments on Original and SWIFT-R protected programs
Schirmeier, Horst, Christoph Borchert, and Olaf Spinczyk. "Avoiding pitfalls in fault-injection based comparison of program susceptibility to soft errors." Dependable Systems and Networks (DSN), 2015 45th Annual IEEE/IFIP International Conference on. IEEE, 2015.

## Slide 8: Reliability is hard to achieve!
“Organization of redundancy and fault-tolerance for ultra-high reliability is a challenging problem: redundancy management can account for half the software in a flight control system and, if less than perfect can itself become the primary source of system failure.”
-- John Rushby https://shemesh.larc.nasa.gov/fm/fm-ft.html

## Slide 9: NEMESIS
Goal: Protecting the execution of all
instructions without any vulnerable window
  M- and D- streams are used for error detection and R-stream is used just for error recovery
  Checking the result of critical instructions instead of their operands
  Error detectors instead of voting-operations
  Off performance-critical-path error handling
M-stream
R-stream
D-stream
      Critical Operation
      Error
      Detector
No Error
Off performance-critical-path error handling
Diagnosis
routine
Memory restoration
Majority-voting
Detected Not-Recoverable
Restart
Recoverable
Error
      Critical Operation

## Slide 10: Error detection on the result of store operations
Main idea: Load back the result of store and check it against redundant version
store Val[Adr]
Val, Adr
Val*, Adr*
M-stream
D-stream
[adr]
Val
Memory
load SCR [Adr*]
if (SCR != Val*) Diagnosis();
Checking the results of store, verifies the execution of store as well as the correct operand computations
Notes: Rather than checking store register operands, NEMESIS detects errors on the results of store

## Slide 11: Challenges in checking the result of Store
store Val[Adr]
Val, Adr
Val*, Adr*
M-stream
D-stream
Errors on address part of silent stores remain undetected.
[adr]
Val
Memory
load SCR [Adr*]
if (SCR != Val*) Diagnosis();
Val
Faulty Address
Store is silent.
(The Store Value is presented in Store target address even before the execution of store)
Undetected
Notes: First lest define silent stores..
On average ~20% of stores are silent

## Slide 12: Solving the problem of Silent Stores
Main idea: Skip over silent stores
Suffer from missing-memory-update errors
Val, Adr
Val*, Adr*
M-stream
D-stream
load SCR  [Adr]
If (SCR == Val) Jump L;
store Val[Adr]
load SCR [Adr*]
L: if (SCR != Val*) Diagnosis();
Silent Store Check
Store Result Check
load VCR  [Adr]
load SCR  [Adr*]
If (SCR == Val)
mov SCR, VCR
Jump L;
store Val[Adr]
mov SCR, VCR
load VCR [Adr*]
L:
if (VCR != Val*) Diagnosis();
Val, Adr
Val*, Adr*
M-stream
D-stream
Silent Store Check
Store Result Check

## Slide 13: Error Diagnosis and recovery on store operations
Why do we need diagnosis routine?
  Inter-stream error propagation
  Unavailable memory backup
    Errors altering store effective address computations
If error is diagnosed as recoverable:
mov Rm, 10
mov Rd, 10
mov Rr, 10
add Rm, Rm, 10
add Rd, Rd, 10
add Rr, Rr, 10
Error alters first add destination register pointer (Rm) to the Rd
Rm = 10
Rd = 30
Rm = 20
Three different values! Voting cannot solve the problem
(1) Restore the state of memory
(2) Masking the effect of error from registers
(3) Program resume by store re-execution

## Slide 14: Error detection on the result of branch operations
BB0
cmp r1, r2
If (cond) .BB1
BB1
BB2
Taken
Not-Taken
BB0
cmp r1, r2
If (cond) .BB1
BB1
BB2
Taken
Not-Taken
cmp r1*, r2*
If (!cond) Diagnosis()
cmp r1*, r2*
If (cond) Diagnosis()
NEMESIS Control-Flow Transformation
Simple Control Flow

## Slide 15: Error detection on the result of branch operations
NEMESIS Control-Flow Transformation
BB1
cmp r1, r2
If (cond) .BB1
cmp r1, r3
If (cond) .BB1
BB1
cmp r1, r2
If (cond) .BB11
cmp r1, r3
If (cond) .BB12
cmp r1*, r2*
If (!cond) . Diagnosis()
Jump BB1
Jump BB1
cmp r1*, r3*
If (!cond) . Diagnosis()
Jump BB1
Jump BB1
Taken
Taken
Fan-in Basic blocks
.BB11
.BB12

## Slide 16: Experimental setup
LLVM 3.7
  NEMESIS was implemented as late backend pass
Gem5 simulator
5 million faults in various components (registerFile, Pipeline registers, FUs, LSQ)

## Slide 17: NEMESIS-protected programs never produce wrong result!
Chart: Number of SDCs
| stringsearch | bitcount | sha | qsort | CRC | FFT | dijkstra | basicmath | rijndeal | blowfish | adpcm-c | adpcm-d | Total
Original | 573 | 8136 | 16029 | 14182 | 64556 | 4217 | 10 | 3124 | 15859 | 14512 | 12979 | 14893 | 169070
SWIFTR | 153 | 5369 | 12384 | 10102 | 14269 | 2677 | 12 | 5769 | 23138 | 10731 | 11996 | 12074 | 108674
Nemesis | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Number of SDCs
| stringsearch | bitcount | sha | qsort | CRC | FFT | dijkstra | basicmath | rijndeal | blowfish | adpcm-c | adpcm-d | Total
Original | 418 | 2486 | 5043 | 1727 | 1500 | 1222 | 170 | 1095 | 3018 | 936 | 3588 | 3928 | 25131
SWIFTR | 70 | 483 | 470 | 3164 | 660 | 105 | 74 | 280 | 90 | 696 | 457 | 127 | 6676
Nemesis | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: 
| stringsearch | bitcount | sha | qsort | CRC | FFT | dijkstra | basicmath | rijndeal | blowfish | adpcm-c | adpcm-d | Total
Original | 854 | 8340 | 11614 | 4552 | 8959 | 8033 | 36 | 4116 | 1030 | 6571 | 4102 | 8404 | 25360
SWIFTR | 191 | 1112 | 909 | 1240 | 661 | 1163 | 7 | 860 | 222 | 599 | 719 | 925 | 3452
Nemesis | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Number of SDCs
| stringsearch | bitcount | sha | qsort | CRC | FFT | dijkstra | basicmath | rijndeal | blowfish | adpcm-c | adpcm-d | Total
Original | 671 | 6319 | 9095 | 1413 | 5696 | 949 | 16 | 1448 | 8441 | 5325 | 6761 | 7870 | 17498
SWIFTR | 94 | 581 | 543 | 644 | 406 | 338 | 2 | 533 | 813 | 249 | 989 | 868 | 1862
Nemesis | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Load-Store Unit
Register file
Pipeline Registers
Functional Units

## Slide 18: Performance Overhead
Chart: Execution time overhead
| stringsearch | bitcount | qsort | sha | CRC | dijkstra | rijndeal | FFT | basicmath | adpcm-c | adpcm-d | avg
ORG | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SWIFT-R | 2.7323 | 2.8073 | 2.1861 | 4.293 | 2.2999 | 3.7505 | 11.7342 | 2.8573 | 2.4944 | 5.6729 | 5.601 | 4.9338
Nemesis | 2.1126 | 1.7456 | 1.7245 | 3.0374 | 1.85 | 2.7992 | 7.1562 | 2.3973 | 1.8448 | 4.4025 | 4.2119 | 3.4051
NEMESIS protected programs are on average around 25% faster than SWIFT-R protected ones.
NEMESIS is faster because:
  Off-performance critical path error recovery
  Relax memory read instruction triplication
Register Hungary benchmarks, i.e., rijndeal and adpcm, show significant slow-down

## Slide 19: Detected but not recoverable errors
Chart: % of detected faults
| stringsearch | bitcount | sha | qsort | CRC | FFT | dijkstra | basicmath | rijndeal | blowfish | adpcm-c | adpcm-d | avg
Recoverable | 25718 | 33199 | 31425 | 29354 | 48936 | 24158 | 18349 | 24584 | 19340 | 43492 | 39200 | 27096 | 364851
Detected/Not-Recoverable | 1190 | 865 | 1739 | 15 | 1928 | 0 | 2 | 1561 | 0 | 29 | 1377 | 1486 | 10192

## Slide 20: Summary
This work
  A compiler technique, named NEMESIS, for fault detection and recovery is proposed
  Safe off-critical-path error recovery
  Checking the results of critical operations rather that their operands
  A CFC mechanism
Future work
  Enhancing the coverage of NEMESIS to permanent errors