## Slide 1
Optimization of Multi-Channel BCH Error Decoding for Common Cases
Russ Dill, Dr. Aviral Shirvastava, Dr. Hyunok Oh
CASES, ESWeek 2015

## Slide 2
Bose-Chaudhuri-Hocquenghem (BCH)
BCH is an Error Correcting Code (ECC) and is used to correct errors in noisy communications channels or storage mediums
Allowing for noise (errors) enables the use of much faster communications channels and much denser storage mediums
Used in:
  Wireless communication links
  NAND flash storage
  Magnetic storage
  On-chip cache memories
  DRAM memory arrays
  Data buses

## Slide 3
BCH Code
BCH is a configurable block based error correcting code (ECC)
  Message is broken into fixed sized blocks and then each block is formed into a codeword
  Redundant bits (ECC) are added to message to generate codeword
  Size of codeword is configurable
  Error correction capability is configurable
  Redundant bits are used by receiver to detect and correct errors

## Slide 4
BCH Decoding
Decoding is broken into 3 independent stages
Errors

## Slide 5
Syndrome Calculation
  Breaks down received codeword into a set of vectors that depend only on the error locations, easiest stage of decoding
  Syndromes evaluate to zero if no errors are present
  Accepts data serially, outputs syndrome vectors once complete

## Slide 6
Generate Error Locator Polynomial
  Uses the syndrome vectors to calculate a polynomial whose roots give the error locations
  Uses iterative algorithm known as Berlekamp-Massey
  Outputs coefficients when complete

## Slide 7
Factoring Error Locator Polynomial
Uses brute force algorithm know as Chien search
Roots give the locations of the errors
Errors in message can now be corrected
Outputs stream indicating error locations, 0 for no error, 1 for error

## Slide 8
Multi-channel BCH Decoding
Multi-channel decoders combine multiple decoders in parallel
  8 syndrome units, 8 error locator units, 8 root solving units
Increases throughput
Can be fed by multiple parallel communications or storage channels
Can be fed by an interleaved code
    Typically used in communications to spread error bursts across multiple blocks
x8

## Slide 9
Related Work
BCH decoding is a heavily researched area
  Invented in 1959, widely used today
Almost all of that research has focused on improving standalone encoders and decoders
Research has concentrated on improvements to both efficiency and throughput
  Bit-parallel operation of syndrome and chien, Hwang (1991)
  Multi-channel operation, Abraham et al. (2010) and Shi et al. (2004)
  Improvements in syndrome computation, Lin and Costello (1983)
  LFSR improvements, Pahri (2004)
  Error locator improvements Jamro (1997)
  Chien efficiency improvements, Chen and Parhi (2004), Yang, Chen, and Chang (2013)

## Slide 10
Our Observation
Most BCH decoder capability goes unused
  Chance of entire decoder being used is 1/30 billion
In multi-channel configuration, on average only 1/3 of decoders are required
  Remaining blocks contain no errors
Eventually, full decoder will still be required
Presents great opportunity for improvement

## Slide 11
Our Approach
Apply ideas to multi-channel decoder
  Allow possibility that not enough hardware is available right now (leads to performance penalty)
  We still include at least 1 full decoder
  Resize remainder of decoders
Syndromes (S) indicate error vs no error
  All channels must undergo syndrome, but we can eliminate later stages
Include arbitrator to select first available unit
Reduced units
Reduce!

## Slide 12
Our Approach
Can we do better?
  After error locator (Σ), we know the error count
  Single error blocks can be solved directly since they are of the form: λ₁x¹ + λ₀
  Create reduced root locator (r) to replace expensive Chien units (C)
  Add second arbitrator to select correct type of root solver based on error count
Simplified units
Simplify!

## Slide 13
Implementing the Reduction in Hardware Blocks
Large percentage of blocks contain zero errors
Calculate the probability that a block contains zero errors based on BER, p, and block size, n:
Choose number of units such that there is only a small chance (miss rate) that insufficient hardware is available
In example on right, 3 error locator units are chosen as there is a less than 2% chance of 4 or more blocks containing errors

## Slide 14
Choosing the Acceptable Performance Penalty
Miss rate is probability that at any given time, insufficient hardware is available
Miss rate is chosen based on trade-off between area savings and performance penalty
Same equations that determine probability of a certain number of errors within a block can be used to calculate the probability of a certain number of blocks containing errors
For our experiments, 2% was chosen as a good balance
  Most gains are seen before the 2% mark
Largest gain
Less reward

## Slide 15
Choosing the Number of Error Locator Units
For each number of possible units, 1…channel count, plot probability that more than that count will be required
Find smallest count m below the 2% threshold
Implement that many error locator units (Σ)
Number of units required increases with targeted Bit Error Rate (BER)
For BER of 5·10-6, only 1 unit is required
For BER of 1·10-4, only 5 units are required

## Slide 16
Architecture of Pooled Decoder
Pooling is used to connect to a full set of inputs to a reduced number of units
Pooled decoder inserts arbitrators between stages
Allows data to flow to first available decoding unit
In case of root solver (C/r), allows arbitrator to choose unit type based on error count
Still requires full set of syndrome units (small overhead)

## Slide 17
Beyond Removing Units, Optimizing Units
Handling blocks with no errors allowed us to remove entire units
Blocks containing 1 error are still a common case
Error count is only known after error locator polynomial step (Σ)
To take advantage of this observation, we need to create special reduced root solvers (r)
Error polynomial will be of the form λ₁x¹ + λ₀
  Full Chien requires: λnxn … λ₃x³ + λ₂x² + λ₁x¹ + λ₀
Direct solution with simple algebra

## Slide 18
Reduced Root Solver
Solve and Simplify
  Negation is a null operation
  λ₀ is always 1
Provides direct, one step method to find root of error locator polynomial in the case of 1 error
However, the solution cannot be used to directly give an integer index to the error location because BCH codes are computed using an algebra known as finite fields
We need to learn a little about finite fields

## Slide 19
Finite Field Arithmetic
A finite field contains a finite set of elements, operations on any two elements produces another element in the field
Elements can be represented in different forms
  Computation typically uses the binary representation of the polynomial form
All operations are performed modulo the generator polynomial, which defines the field
Moving from the polynomial form to the power form (index) is O(n) where n is the number of elements in the field (Typically in the thousands). Very costly

## Slide 20
Finite Field Addition
Polynomials are added similarly to normal algebra
    (x² + x) + (x + 1) = x² + 2x + 1
But the coefficient of each term is taken modulo the characteristic of the field, which for binary fields is 2, GF(2n)
x² + 2x + 1 = x² + 0x + 1 = x² + 1
This is the same as taking the XOR of the binary representation of the polynomial form
Addition is easy in finite fields!
Subtraction is defined to be the same as addition in finite fields (Negation is a null operation)
Addition:
x² + x
± x + 1
x² + x + 1 → x² + 1
110
xor 011
101

## Slide 21
Finite Field Multiplication
To multiply two elements in power form, just add the exponents modulo the size of the field
  x³ + x⁴ = x(3+4)%7 = x⁰
Multiplication in polynomial form is performed similarly to normal algebra, but taken modulo the generator polynomial:
(x + 1)(x² + x) = x³ + 2x² + x = x³ + x
And then to take it modulo the generator polynomial, we subtract it out:
(x³ + x) – (x³ + x + 1) = 1

## Slide 22
Reduced Root Solver
Observation – we still need to cycle through each bit in the error output (Decoder streams error locations serially)
Rework equation again
Load register with λ₁
Multiply by x¹ each cycle
When register contains 1, we have multiplied by the correct power of x
We have counted the correct number of cycles and have reached the root/error location
Implement with LFSR, extends cheaply to multi-bit support

## Slide 23
Usage of Linear Feedback Shift Register (LFSR)
Multiplies element by x¹, looping through the table
Operates on binary representation
Step 1: shift elements one to the left
Step 2: subtract generator polynomial if needed
x³ + 0x² + x + 1
LFSR can be modified with input/output
  Multiply two values serially
  Divide two values serially, producing a quotient and remainder
Used for many BCH operations
×
o
o
Generator polynomial

## Slide 24
Comparison with Chien Search
Brute force method of finding roots
Loads registers with coefficients (λn) at first cycle (mux used to select)
Multiplies by αn (constant) each subsequent cycle
  n indicates coefficient index
t (number of errors that can be corrected) blocks are required per channel, which is also the number of coefficients
Requires t registers, muxes, and parallel multipliers. Expensive
Sums output of all blocks and compares result with 0 to detect roots
Portion of Chien root finder,
duplicated t times

## Slide 25
Comparison with Chien Search
Bit-parallel operation is scales at a rate beyond linear because of long delays and fanout requiring register duplication
Diagram demonstrates hardware necessary to operate on 8 bits in parallel
Parallel implementation of reduced root solver only requires 1 LFSR
  Output of LFSR is compared against 8 constants per cycle
  LFSR is advanced 8 steps per cycle
9 multipliers
2 multiplexers
2 registers
× t

## Slide 26
Choosing the Correct Number of Root Solvers
Similar to calculation of number of error locator units required
Instead we looks at blocks with more than 1 error (instead of 1 or more)
  Blocks with 1 error can be served by reduced root solver
  Blocks with more errors need Chien search
Calculate probability that more that m Chien units will be required
Plot and choose minimum number of units below 2% threshold

## Slide 27
Experimental Setup
Implemented pipelined BCH decoding architecture in Verilog (baseline)
Target Virtex-6 FPGA, 200MHz timing for comparisons
Create pooled architecture with arbitrators
Make parameters compile time configurable for testing many configurations
Run Place & Route of design for the target, examine results to determine area for the chosen parameters

## Slide 28
Area Optimized Decoder Results
Results of applying our ideas to a set of multi-channel BCH decoder configurations
We allow a 2% performance impact
We gain
  47%-71% area savings
  44%-59% dynamic power savings

## Slide 29
Increasing Throughput
Fit more powerful optimized decoder in area of baseline decoder
Find highest bit-parallel level of optimized decoder that fits within area of baseline decoder
  Each channel within baseline decoder operates on 4 bits
  Increasing bit-parallel capability of each channel increases throughput, but grows area
  Optimized version of decoder gives us plenty of headroom to grow!
300%-500% increase in throughput!

## Slide 30
How Multi-Bit Increases Throughput
Computing error locator polynomial does not need to be modified for multi-bit support
Syndrome computation streams input data, limits throughput
  Syndrome computation is typically performed via LFSR, which scales well to bit-parallel operation
Root solver streams error locations as output, limits throughput
  Increasing Chien search to bit-parallel operation involves duplicating multipliers, muxes and registers
  Including many multipliers lead to timing problems requiring register duplication, resulting in even more area
  Our reduced root solver is simply an LFSR and extends well to bit-parallel operation

## Slide 31
Extending Flash Lifetime
Optimization savings allow us to implement a more powerful decoder in the same area
Find optimized decoder with largest targeted Bit Error Rate (BER) that fits into the area of the baseline decoder
We can now support an increased lifetime for flash memory, whose error rate increases as it ages
We are able to achieve a 1.4x-4.5x increase in flash lifetime

## Slide 32
Flash Lifetime Background
P/E cycles cause flash memory to wear
Decreasing process sizes cause wear to happen sooner
Flash manufacturers recommend an ECC strength in bits to reach a specified flash lifetime
ECC strength chosen is a trade-off based on decoder requirements
By providing more ECC strength in a same sized decoder, we can change that trade-off
Cai et al. (2012) shows age/BER generally follows the relation:

## Slide 33
Conclusions
We examined possibilities for improving multi-channel BCH decoders
By allowing a 2% performance degradation, we experienced massive gains, 47%-71% area savings, 44%-59% dynamic power savings.
We can fit faster and more powerful optimized decoders in the same area of the baseline decoder
  3x-5x increase in throughput
  1.4x-4.5x increase in flash lifetime

## Slide 34
Questions?