## Slide 1: Maintaining Sanity: Algorithm-based Comprehensive Fault Tolerance for CNNs
Jinhyo Jung*, Hwisoo So#, Woobin Ko*, Sumedh Joshi#, Yebon Kim*, Yohan Ko*, Aviral Shrivastava#, Kyoungwoo Lee*
* Yonsei University, # Arizona State University
Presented by Jinhyo Jung
Paper #379

## Slide 2: Reliability: a Key Design Concern
Reliable protection technique for CNNs required
  CNNs now being applied even in safety-critical applications
Transient faults pose significant threat to reliability
  Transient faults: temporary system glitch caused by hardware/network issues
Autonomous Vehicles
Aerospace Applications
Disease Diagnosis

## Slide 3: Previous Methods: Modular Redundancy
Makes redundant copies of the system to detect/correct faults
Hard to apply in resource-constrained environments due to high overheads
Voter
Triple Modular Redundancy
Fault Corrected
Comparator
Dual Modular Redundancy
Fault Detected

## Slide 4: Previous Methods: Sanity-Check [Ozen, ATS ‘19]

## Slide 5: Previous Methods: Sanity-Check [Ozen, ATS ‘19]

## Slide 6: Previous Methods: Sanity-Check [Ozen, ATS ‘19]
Fault detected through checksum
Fault in parameter only affects one output
Possible correction with fault location

## Slide 7: Maintaining Sanity: Overview
Categorize data to model parameters and layer inputs
  Apply checksum-based protection to correct faults in model parameter faults
  Apply redundancy-based protection to correct faults in layer inputs

## Slide 8: Model Parameter Redundancy: FC Layer
Detect fault using Total Sanity Checksum
Correct fault using ABFT-based equation
Error detection patterns of Partial Sanity Checksums |  |  |  |  |  |  | 
Error detection patterns of Partial Sanity Checksums |  |  |  |  |  |  | 
Locate fault using Partial Sanity Checksums
Requires additional partial sanity neurons

## Slide 9: Model Parameter Redundancy: Conv Layer
Addition of partial sanity filters
Detect fault with Total Sanity Checksum
Locate fault with Partial Sanity Checksums
Correct fault using the ABFT-based equation

## Slide 10: Layer Input Redundancy
Dual Modular Redundancy to detect faults
  Checksum method requires use of batch inputs
  Cannot provide fast recovery
Duplicate only the original input to network
  Each duplication induces single-point-of-failure
  Minimize window of vulnerability
Checkpoint and rollback to correct error
  Intertwine check and store to eliminate vulnerability

## Slide 11: Experimental Setup
Target CNNs
  LeNet-5 pretrained on MNIST
  AlexNet, ResNet18, VGG16 pretrained on ImageNet
Implemented in PyTorch using float32, run in Intel Xeon 2.2GHz CPU
Error model
  Inject one bit-flip per run to collect cases of classification faults (critical faults)
  Check if protection technique detects/corrects critical faults

## Slide 12: Experimental Setup: Baseline Techniques
N-TMR(Network-level TMR)
  Triplicate entire network and input
I-TMR(Input-level TMR)
  Triplicate only the input
Spa-SC(Spatial-only Sanity-Check)
  Sanity-Check w/o input redundancy
SC(Sanity-Check)
  Sanity-Check implemented for single-inputs
MS(Maintaining Sanity)
  Our technique
I-TMR
N-TMR
Spa-SC
SC
MS

## Slide 13: Results: Coverage and Runtime

## Slide 14: Results: Memory Costs
Memory Costs
  MS requires less than 10% additional parameters for LeNet5
  Normalized overhead decreases as model size increases

## Slide 15: Summary
Maintaining Sanity
  Checksum-based protection for layer parameter faults
  Duplication-based protection for layer input faults
Almost perfect fault coverage with 135% runtime overhead and minimal additional memory costs
27% lower runtime overhead compared to full triple modular redundancy
  Other techniques that are faster suffer from incomprehensive coverage