## Slide 1: RIM: Robust Intersection Management for Connected Autonomous Vehicles
Mohammad Khayatian, Mohammadreza Mehrabian, Aviral Shrivastava
Arizona State University
Notes: Hello everyone,
My name is Mohammad Khayatian and I’m a PhD student at ASU. Today, I will present our work on Robust intersection management of Connected Autonomous vehicle.

## Slide 2: Why Autonomous intersections?
Accidents at intersection
  Between 2010 and 2015 , around 30% of fatal crashes have happened in intersection areas, most of which, involved human errors. [FHA]
Traffic Congestion
  On the average, each person in the US spends around 42 hours per year stuck in the traffic [FHA]
As cars become autonomous, so too can intersections
  Intersection Management using V2I
[FHA] Roadway Safety Data Dashboards, US Department of Transportation - Federal Highway Administration
Notes: 1) Why do we need automated intersections?
2) Let’s start with some statistic:
3) According to the Federal Highway administration, About 30% of fatal accidents has happened in intersection area and most of which involved human errors.
Click.
4) Believe me, you don’t wanna be in any of those cars.
5) Also, on the average, each person in the US spends around 42 hours per year stuck in the traffic
6) These two issues, highlight the need for automation.

## Slide 3: Intersection Manager (IM)
An infrastructure communicating with incoming vehicles.
Contains Multiple computing systems
Real-time communication
Real-time actuation
  Safety
  Robustness
Intersection Manager
Notes: 1) Implementing a safe autonomous intersection manager is challenging.
2) Because there are multiple computing systems that communicates with each other
3) and, real-time communication, processing and actuation is required.

## Slide 4: Safety buffer
IM should consider a safety buffer around each vehicle to account for uncertainties in vehicles position
Localization of autonomous vehicle is challenging
Notes: The most important aspect of intersection management is safety.
Since localization is not perfect, IM needs to account for uncertainties in the position by considering a safety buffer around a car.

## Slide 5: Existing Approaches
Query-based Intersection Management (QB-IM)
  Vehicles send estimated time of arrival and velocity of arrival to IM
  IM accepts/rejects the request
  AIM (Autonomous Intersection Management) [1]
Velocity Assignment Intersection Management (VA-IM)
  Vehicles send their position and velocity
  A target velocity is assigned to the vehicle
  Cooperative Vehicle Intersection Control (CVIC) [2]
[1] Dresner, Kurt, and Peter Stone. "A multiagent approach to autonomous intersection management." Journal of artificial intelligence research 31 (2008): 591-656.
[2] Lee, Joyoung, and Byungkyu Park. "Development and evaluation of a cooperative vehicle intersection control algorithm under the connected vehicles environment." IEEE Transactions on Intelligent Transportation Systems 13.1 (2012): 81-90.
Notes: 1) Many intersection management techniques have been proposed so far.
2) and we categorize them as Query-based approaches or QB-IM and Velocity assignment approaches or VA-IM.
3) In Query-based approaches, a vehicle that approaches the intersection, sends its estimated time of arrival and velocity of arrival to the IM
4) and, IM simulate the future trajectory of the vehicle inside the intersection and accordingly, replies a Yes to the vehicle if the trajectory doesn’t have any conflicts with existing vehicles is safe.

## Slide 6: QB-IM (Query-based Intersection Management)
Intersection Manager
Request Line
Enter
Exit
t=0
t=1
t=2
t=4
t=5
t=6
t=3
t=7
yes
[1] Dresner, Kurt, and Peter Stone. "A multiagent approach to autonomous intersection management." Journal of artificial intelligence research 31 (2008): 591-656.
Not efficient

## Slide 7: VA-IM (Velocity Assignment Intersection Management)
Intersection Manager
Request Line
Enter
Exit
10.2 m/s
8.5 m/s
[1] Lee, Joyoung, and Byungkyu Park. "Development and evaluation of a cooperative vehicle intersection control algorithm under the connected vehicles environment." IEEE Transactions on Intelligent Transportation Systems 13.1 (2012): 81-90.
Better Efficiency

## Slide 8: Timing Problem in VA-IM
Round Trip Delay (RTD) due to communication is ignored.
  Inconsistency between vehicle position and what IM thinks
Actual Receive
Position
Best
Average
Worst
Request Line
Expected Receive Position
Worst-case error in position ()
IM

## Slide 9: Ignoring RTD Will Cause Crashes
Intersection Manager
Request Line
Accidents will happen!

## Slide 10: Crossroads Technique
IM sets the execution location to be a fixed value as:
Best
Worst
Request Position
IM
Actuation Position
Actuation Begins…
Actuation Begins…
b
[1] Andert, Edward, Mohammad Khayatian, and Aviral Shrivastava. "Crossroads: Time-Sensitive Autonomous Intersection Management Technique." Proceedings of the 54th Annual Design Automation Conference 2017. ACM, 2017.

## Slide 11: Issues of Crossroads
Safety-related
  1) Vehicles are assumed to have zero actuation time
  2) Assigned velocity will be maintained until entering the intersection
  What if a disturbance is applied to the vehicle?
  Wind, bump, etc.
Request Line
Actuation Position
Edge of the intersection
Target Velocity
time
Velocity
Request Line
Actuation Position
Edge of the intersection
Target Velocity
time
Velocity

## Slide 12: Issues of Crossroads
Low Performance
  A constant Velocity is assigned.
  To avoid rollover, turn speed is low.
  Vehicles that intend to make a turn will slow down others.

## Slide 13: RIM Overview
Request Line
Intersection Manager
Request
Response
Synchronization Line
Phase 1
Phase 2
Phase 3
Phase 4
Sync
Request
TOA & VOA
VOA
Velocity
time
Track the trajectory
Find the optimal trajectory
TOA
Maintain the velocity

## Slide 14: Our Approach: RIM
1) Clock Sync
3) Send a request to IM
8) Find an optimal trajectory
9) Inform IM
9) Track the trajectory
2) Clock Sync
4) Checks for conflicts
5) Check the feasibility
6) Send TOA and VOA
11) Store it.
Vehicle
IM

## Slide 15: Find the Optimal Trajectory
We define a functional based on acceleration:
Solve using Fundamental Lemma of the Calculus Variation:
Linear acceleration is optimal!

## Slide 16: Find the Optimal Trajectory (cont.)
Taking integral from acceleration we have:
Taking integral from velocity we have:
Substituting the initial and final conditions (, we have:

## Slide 17: Dealing with Round-trip Delay
As soon as TOA and VOA are received, the optimal trajectory is determined.
All determined trajectories will meet the TOA and VOA requirement.
Vehicles will control the position instead of velocity
Request Time

## Slide 18: Feasibility of VOA and TOA
Is the assigned TOA and VOA feasible?
Min and max acceleration rates
  Vehicles have limited acc/dec power
Min and max velocities
  Road speed limit

## Slide 19: Feasibility of VOA and TOA
Request line

## Slide 20: Our Testbed
4-way intersection
1/10 scale RC cars on Traxxas chassis
Vehicle size = 30 cm x 57 cm max speed = 5 m/s (11.1 mph)
Lane width = 60 cm
Transmit line distance = 3 m
NTP protocol for clock synchronization (10 ms accuracy)
PID controller for position trajectory tracking
3 types of communication packets
  Sync (7 Bytes), Request (30 Bytes), Receive (30 Bytes)

## Slide 21: IM & Car Schematic
Main uC
Transceiver
1st uC
2nd uC
LIDAR
IMU
GPS
Motor
Encoder
Wireless
USART
USART
Square Wave
Servo
Motor
PWM
PWM
Autonomous Car
IM
Transceiver
IM uC
SPI
SPI

## Slide 22: Video of Our Intersection

## Slide 23: Crossroad Position Error
Chart: Time (s)
Chart: Time (s)
Disturbance is applied
Model Mismatch Error
External Disturbance Error
Actuation time
Position Error
Edge of the intersection
10 % model mismatch is added.
An external disturbance of 5% is applied
Monitor position and velocity of a CAV.

## Slide 24: RIM is Robust
Chart: TRAJECTORIES IN PRESENCE OF MODEL MISMATCH AND EXTERNAL DISTURBANCE
Chart: Time (s)
Disturbance is applied
Receive time
10 % model mismatch is added.
An external disturbance of 5% is applied
Monitor position and velocity of a CAV.
Almost zero error
Edge of the intersection

## Slide 25: Robustness of RIM vs Crossroads
Chart: Position Error in presence of Model Mismatches and External Disturbances
| Model Mismatch (MM) | External Disturbance (ED) | MM + ED
AVG Crossroads | 0.61389 | 0.66401 | 1.2767
MAX Crossroads | 1.731 | 1.5998 | 3.3282
AVG RIM | 0.04 | 0.033 | 0.073
MAX RIM | 0.0695 | 0.069667 | 0.13917
We repeated our experiment 50 times. For different VOA and TOA
3.3X!
14%

## Slide 26: Crossroads needs a Safety Buffer
Since Crossroads does not consider model mismatches and external disturbances, it’s not safe!
However, Crossroads can still work if we consider a safety buffer of 3.3X of size of the car.

## Slide 27: Evaluation using Our Simulator
Developed in MATLAB® [1]
Scale to multi-lane intersection
Variable traffic flow rates
Model vehicle dynamics
Model network delay
[1] Available Online: https://github.com/mkhayatian/Traffic-Intersection-Simulator-for-Autonomous-Vehicles

## Slide 28: Simulator Video
Available Online: https://github.com/mkhayatian/Traffic-Intersection-Simulator-for-Autonomous-Vehicles

## Slide 29: Throughput Improvement
Chart: FLOW RATE (VEHICLE PER LANE PER SECOND)
| 0.1 | 0.09 | 0.08 | 7.0000000000000007E-2 | 0.06 | 0.05 | 3.9999999999999897E-2 | 2.9999999999999898E-2 | 1.99999999999999E-2 | 9.99999999999991E-3
3 Lane intersection | 0.082692 | 0.060972 | 0.034328 | 0.0051171 | 0.004759 | 0.0044662 | 0.0029959 | 0.0023852 | 0.0017582 | 0
Single lane intersection | 0.055 | 0.033 | 0.022 | 0.009 | 0.004759 | 0.0044662 | 0.0029959 | 0.0023852 | 0.0017582 | 0

## Slide 30: Efficiently Making a Turn
Chart: Speedup in Throughput for different turn velocity limits
| 0.4 | 0.6 | 0.8 | 1 | 1.2 | 1.4 | AVG
RIM | 8 | 5.4286 | 2.8571 | 2.0865 | 1.3158 | 1.2261 | 2.5828
Crossroads | 1 | 1 | 1 | 1 | 1 | 1 | 1
Crossroads & VA-IM
  A constant Velocity is assigned.
  To avoid rollover, turn speed is low.
  Vehicles that intend to make a turn will slow down behind vehicles.
RIM
  Vehicles can adjust their speed.

## Slide 31: Position of Our Work
Query-based (AIM)
Velocity Assignment
Expected
Time of Arrival &
Velocity of Arrival
Accept or Reject
QB-IM
VA-IM
Crossroads
Assigned Velocity
Current Velocity & Position
②
②
②
①
①
①
Current Velocity,
Position & Timestamp
Assigned Velocity & Actuation timestamp
RIM
②
①
Current Velocity,
Position & Timestamp
Time of Arrival & Velocity of Arrival
Crossroads
RIM

## Slide 32: Conclusion
We explored safety concerns of previous intersection management techniques.
  Network delay
  Vehicle dynamics
We presented a robust intersection management interface for connected autonomous vehicles.
  Model mismatch
  External disturbances
  Efficient

## Slide 33: Question?
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 34: Finding with WCRTD
Timeout when delay is large and stop the vehicle.
  Not working is better than causing an accident!
Usual delay
Timed out
Selected Threshold

## Slide 35: Round-trip Delay
The Worst-case RTD = WCET + WCND
  Worst case network delay in the forward and backward paths
  Worst-case execution time of the IM
WCND
  Nondeterministic (theoretically infinite!)
WCET
  Measurement-based methods (No guarantee)
  Static methods (pessimistic)
Therefore, WCRTD cannot be determined and compensated!