## Slide 1: InCheck – An Integrated Recovery Methodology for nZDC
Dheeraj Lokam
Compiler Microarchitecture Lab
Arizona State University

## Slide 3: Key Takeaways
Implementing light weight checkpointing at assembly level
Accomplishing a quick recovery on top of an existing detection scheme
A recovery methodology with near zero failure rate

## Slide 4: Reliability is a first class design concern:
Aggressive transistor feature scale down rendered processors to become more and more susceptible to Soft-Errors.
  Typically cause by cosmic particle strikes
Transient Errors/LETs are a major threat to system reliability
  Silent Data Corruptions
  System Hangs
  Segmentation Faults
Silent Data Corruptions (SDC) are the most difficult errors to catch
  They don’t generate any symptom
  Undetectable by simple hardware/software detectors
0
1

## Slide 5: Why Software Level Techniques?
Flexibility
  They can optimized based on the workload characteristics without having to change the hardware
Coverage
  There are software techniques that can provide near zero SDC
    Eg. nZDC
Cheap
  They can be implemented on any off-the-shelf processor
Software level techniques can now be used
to protect any application from soft-errors

## Slide 6: Soft-Error detection through Software
Core 1
Full duplication should detect almost all soft-errors
Can be done at multiple levels of abstraction
  Process-level duplication
  Assembly-level Instruction duplication
    Provides fine details of actual execution
    Easy to optimize
  Coarse-grained approach
  Fine-grained approach
Core 2
Process A
Process A*
comparator

## Slide 7: Software Implemented Detection
Error Detected?
Re-execute
Main Stream
Shadow
In many real-life applications, restart is not an option!
  Interactive applications
  Applications with considerably long execution times

## Slide 8: Recovery by Triplication
Majority Voting
Main Stream
Shadow1
Shadow2

## Slide 9: Implementing recovery on top of detection is tricky
Improperly done Triplication could jeopardize detection’s fault coverage:
  Majority voting becomes a single point of failure
  Adding more instructions within vulnerable windows makes things worse
Lessons learnt from the past!
    Transforming SWIFT to SWIFT-R compromises the error coverage

## Slide 10: SWIFT is not effective!
cmp x1, x1*
b.ne error
load x2, [x1]
mov x2*, x2
mov x1, #0x04
mov x1*, #0x04
add x2, x2, #0x10
add x2*, x2*, #0x10
and x1, x2, #0x10
and x1*, x2*, #0x10
cmp x2, x2*
b.ne error
cmp x1, x1*
b.ne error
store x2, [x1]
mov
mov
store
add
add
and
and
= Vulnerable
= Protected
load
Checking Value
Load value duplication
Checking Address
Checking Value
mov x1, #0x04
load x2, [x1]
add x2, x2, #0x10
and x1, x2, #0x10
store x2, [x1]
Original Code

## Slide 11: SWIFT-R makes things worse!
majority_voting (x1, x1*, x1**)
load x2, [x1]
mov x2*, x2
mov x2**,x2
mov x1, #0x04
mov x1*, #0x04
mov x1**, #0x04
add x2, x2, #0x10
add x2*, x2*, #0x10
add x2**, x2**, #0x10
and x1, x2, #0x10
and x1*, x2*, #0x10
and x1**, x2**, #0x10
majority_voting (x2, x2*, x2**)
majority_voting(x1, x1*, x1**)
store x2, [x1]
= Vulnerable
= Protected
mov
mov
store
add
add
and
and
load
Checking Value
Load value duplication
Checking Address
Checking Value
mov
Checking Value
Checking Value
add
and
Checking Address
Checking Address
Checking Value
Checking Value
mov
mov
store
add
add
and
and
load
Checking Value
Load value duplication
Checking Address
Checking Value
majority_voting (R, R*, R**)
cmp R, R*
b.ne recover from R**
cmp R,R**
b.ne recover from R*
cmp R*,R**
b.ne recover from R
cmp x1, x1*
b.ne error
load x2, [x1]
mov x2*, x2
mov x1, #0x04
mov x1*, #0x04
add x2, x2, #0x10
add x2*, x2*, #0x10
and x1, x2, #0x10
and x1*, x2*, #0x10
cmp x2, x2*
b.ne error
cmp x1, x1*
b.ne error
store x2, [x1]
SWIFT
SWIFT-R

## Slide 12: SWIFT vs SWIFT-R SDC Distribution
Chart: Number of SDCs
| stringsearch | bitcount | sha | qsort | crc32 | fft | basicmath | rijndael | blowfish | Total
SWIFT | 1 | 19.2 | 3 | 2 | 7 | 4 | 67.2 | 6 | 8 | 117.4
SWIFT-R | 38.4 | 281.28 | 273.6 | 1790.4 | 469.44 | 69.12 | 199.68 | 53.76 | 393.6 | 3569.28
10,000 experiments per benchmark

## Slide 13: Recovery by checkpointing:
Error Detected?
Main Stream
Shadow
check-point

## Slide 14: Lessons learnt from prior checkpointing approaches
Coarse grained approaches pause the execution to make checkpoints.
  More Storage space needed – 0.5-1 GB *
  Most HPC facilities spend almost half their time in checkpointing **
Fine-grained checkpointing were proposed by integrating checkpointing into the application itself.
  Storage space needed for checkpointing – in the order of bytes
  Checkpointing overhead – in the order of ns
  Recovery time can be more deterministic and quick
Existing methods of fine-grained checkpointing could not produce guaranteed recovery. Eg: FASER
  Unsafe Checkpointing
  Unsafe recovery
* Dong, Xiangyu, et al. "A case study of incremental and background hybrid in-memory checkpointing." Proc. of the 2010 Exascale Evaluation and Research Techniques Workshop. Vol. 115. 2010.
**Elmootazbellah N Elnozahy and James S Plank. Checkpointing for
peta-scale systems: A look into the future of practical rollback-recovery.
IEEE Transactions on Dependable and Secure Computing, 1(2):97–
108, 2004.

## Slide 15: FASER* - Fine-grained Soft-Error Recovery
Inherits all the vulnerabilities from SWIFT.
Xu, Jianjun, et al. "An instruction-level fine-grained recovery approach for soft errors." Proceedings of the 28th Annual ACM Symposium on Applied Computing. ACM, 2013.
cmp R1, R1*
b.ne error
load R2, [R1]
mov R2*, R2
add R2, R2, #0x10
add R2*, R2*, #0x10
SWIFT Basic Block
FASER Basic Block
Save_BB_label
cmp R1, R1*
b.ne error
load R2, [R1]
mov R2*, R2
add R2, R2, #0x10
add R2*, R2*, #0x10
cmp R2, R2*
b.ne error
mov chkpt_reg, R2

## Slide 16: Goal of InCheck:
Integrating recovery on top of a detection technique,
  Without compromising the coverage provided by detection
  With a low recovery latency
Recent work, nZDC could accomplish near Zero SDC by detecting every error. So, it was chosen as the candidate to implement InCheck Recovery.

## Slide 17: nZDC: Compiler transformations for complete protection from SDC
nZDC could accomplish full instruction duplication
  Logical and Computational Instructions
  Memory read instructions
  Memory write instructions!
    Checking load instructions act as duplication for Stores
  Compare instructions
    Duplicated by nZDC CFC
  Branch instructions
    Direction as well as target address checking
nZDC could achieve its goal
  Near zero Silent Data Corruption at Processor Level
  nZDC protected programs execute faster than their SWIFT counterparts

## Slide 18: nZDC transformations:
Un-Reliable Code
mov x1, #0x04
load x2, [x1]
add x2, x2, #0x10
and x1, x2, #0x10
store x2, [x1]
nZDC transformation
mov x1, #0x04
mov x1*, #0x04
load x2, [x1]
load x2*, [x1*]
add x2, x2, #0x10
add x2*, x2*, #0x10
and x1, x2, #0x10
and x1*, x2*, #0x10
store x2, [x1]
load x2, [x1*]
cmp x2, x2*
b.ne error

## Slide 19: InCheck + nZDC:
InCheck is a fine-grained technique that performs recovery by
making light weight checkpoints
Detection Mechanism
Error Diagnosis Mechanism
Recovery Mechanism
Detected/
Unrecoverable
InCheck performs recovery only when it’s sure that its going to be error-free.
error detected?
error recoverable?
Yes
No
check-
pointing
redundant execution

## Slide 20: InCheck Transformation:
Register File Preservation
Memory Preservation
Checkpoint Error Detection
Control Flow Error Check
CHECK POINTING
main thread
shadow thread
Error detected?
Redundant Execution
nZDC Basic block:
nZDC error detected!
Restart
Recovery
Memory Restore
Register File Restore
InCheck Basic block:

## Slide 21: Key Features of Recovery
Memory preservation and Restoration
2 Phase Checkpointing
Recovery from CF errors

## Slide 22: Need for Memory Preservation & Restoration:
BB: load R1 <- [R2] load R1* <- [R2*] R1++
R1*++ store R1 -> [R2] load R1 <- [R2*] cmp R1, R1* b.ne recovery
register recovery:
load R1 <- [memory] load R2 <- [memory, #4] branch to BB
BB: load R1 <- [R2] load R1* <- [R2*] R1++
R1*++
store R1 -> [R2] load R1 <- [R2*] cmp R1, R1* b.ne recovery
memory recovery:
restore([R2])
register recovery:
restore R2 branch to BB
Original program
First-cut recovery scheme (with register restoration only)
InCheck recovery (with memory and register restoration)
preserve (R2)
preserve (R2)
preserve ([R2])
10
10
11
10
10
16
[R2]
16
16
17
In recovery block, R2 is loaded with correct initial address but [R2] remains un-restored
load R1 <- [R2]
R1++
store R1 -> [R2]
10
10
16
[R2]
10
10
11
In recovery block, [R2] is re-loaded with its initial value before store operation
[R2]
recovery:
recovery:
Soft-error happens on R1
Soft-error happens on R1
Q
P
Value in memory location [R2]:
checkpoint:
checkpoint:

## Slide 23: 2 Phase Checkpointing:
Register File Preservation
Checkpoint Error Detection
Error detected?
Check pointing to mem. A:
Restore from check pointing memory B
Jump back to beginning of prev. BB
Restore from check pointing memory A
Re-execute from the beginning of current BB
Register File Preservation
Checkpoint Error Detection
Error detected?
Check pointing to mem. B:
Intra block Recovery:
Inter block Recovery:
Restore from check pointing memory A
Jump back to beginning of prev. BB
Restore from check pointing memory B
Re-execute from the beginning of current BB
Intra block Recovery:
Inter block Recovery:
main thread
shadow thread
Error detected?
Redundant Execution
BB1
BB2
main thread
shadow thread
Error detected?
Redundant Execution
Memory A
Memory B
Memory A
Memory B
Memory A
Memory B
Memory A
Memory B

## Slide 24: Recovery from Control Flow Errors:
Check pointing:
main thread
shadow thread
recovery:
BB 2:
Check pointing:
main thread
shadow thread
BB 1:
cond. branch BB 2
Redundant computation
Redundant computation
Check pointing:
main thread
shadow thread
BB 3:
cond. branch BB 2
Redundant computation
step-1:Restore Registers & memory step-2: Jump back to label address stored in label_reg
nZDC Control Flow Error Detection:
CF error detected? -> exit( )
Register File Preservation
Checkpoint Error Detection
Control Flow Error Detection
  if error detected?
Register File Preservation
Checkpoint Error Detection
Save label addr. of current BB
Register File Preservation
Checkpoint Error Detection
Save label addr. of current BB
main thread
shadow thread
BB 3:
cond. branch BB 2
Redundant computation
main thread
shadow thread
BB 1:
cond. branch BB 2
Redundant computation
main thread
shadow thread
BB 2:
Redundant computation
nZDC Control Flow Error Detection:
CF error detected? -> exit( )
nZDC
nZDC + InCheck

## Slide 25: Experimental Setup
ARM cortex A-53 like micro-processor simulated in gem5
Parameter | Value
CPU Model | ARM64 bit in-order processor
Pipeline | Two way/4-stage
Number of FUs | 2Int, 1Mul, 1Div, 1Float, 1Mem
L1 D/I-Cache | 64KB(2-way) / 32KB (2-way)
TLB Size | 512 entries
Integer registerfile | 32 registers (64-bit width)
Store Buffer Size | 5 entries

## Slide 26: Experimental Setup
Processor Components subjected to FI
  Register File
  Load Store Queue
  Pipeline Registers
  Functional Unit
6 benchmarks from MiBench were subjected to FI
72,000 Faults Injection Experiments Overall
  12,000 FI Experiments per benchmark for all 4 components
    3000 FI Experiments per component per benchmark
95% confidence level and 1% error margin

## Slide 27: Understanding Results:
ARM Cortex
A 53
Recognizable Change
in program behaviour
SDC
Un-Recognizable Change
in program behaviour
No Change
in program behaviour
Segmentation Fault
Program Abort
Masked
Recovered
Detected/Not-Recoverable
*For InCheck only

## Slide 28: SDC Distribution in Processor-wide Fault Injection Experiments
Processor components subjected to FI
  Register File
  Load Store Queue
  Pipeline Registers
  Functional Units
72,000 Random Faults Overall
  12,000 per benchmark
    3000 per component in each benchmark
1% Error Margin
95% Confidence
Chart: Number of SDCs
| stringsearch | qsort | bitcount | crc32 | sha | fft | TOTAL
Original | 139.2 | 995.1 | 1068 | 2398.2 | 1911.9 | 1277.1 | 7789.5
SWIFT-R | 45.3 | 882.6 | 259.8 | 340.8 | 369.9 | 233.4 | 2131.8
InCheck | 0 | 0 | 0 | 0 | 0 | 0 | 0
0
ARM Cortex
A 53
Recognizable Change
in program behaviour
SDC
Un-Recognizable Change
in program behaviour
No Change
in program behaviour
Segmentation Fault
Program Abort
Masked
Recovered
Detected/Not-Recoverable
*For InCheck only

## Slide 29: SDC Distribution in Component-wise Fault Injection Experiments
Chart: Pipeline Registers
| stringsearch | qsort | bitcount | crc32 | sha | fft | TOTAL
Original | 21.9 | 439.2 | 298.2 | 1481.7 | 277.8 | 975.3 | 3494.1
SWIFT-R | 25.8 | 168 | 98.1 | 110.1 | 172.5 | 177.3 | 751.8
InCheck | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Register File
| stringsearch | qsort | bitcount | crc32 | sha | fft | TOTAL
Original | 76.5 | 298.5 | 438.6 | 287.7 | 927.6 | 222.6 | 2251.5
SWIFT-R | 12.3 | 559.5 | 87.9 | 146.7 | 85.5 | 21.6 | 913.5
InCheck | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Load-Store Unit
| stringsearch | qsort | bitcount | crc32 | sha | fft | TOTAL
Original | 12.6 | 177 | 45.6 | 300 | 211.2 | 37.5 | 783.9
SWIFT-R | 1.5 | 50.4 | 19.8 | 56.1 | 75.6 | 9.6 | 213
InCheck | 0 | 0 | 0 | 0 | 0 | 0 | 0
Chart: Functional Unit
| stringsearch | qsort | bitcount | crc32 | sha | fft | TOTAL
Original | 28.2 | 80.4 | 285.6 | 328.8 | 495.3 | 41.7 | 1260
SWIFT-R | 5.7 | 104.7 | 54 | 27.9 | 36.3 | 24.9 | 253.5
InCheck | 0 | 0 | 0 | 0 | 0 | 0 | 0
0
0
0
0

## Slide 30: Recoverable & UnRecoverable Errors in InCheck
Chart: Percentage Errors (%)
| stringsearch | qsort | bitcount | crc32 | sha | fft | AVERAGE
Recovered | 0.9 | 0.9236 | 0.9817 | 0.9743 | 0.9542 | 0.9631 | 0.94948
Detected/UnRecoverable | 0.1 | 0.0764 | 0.0183 | 0.0257 | 0.0458 | 0.0369 | 0.050517

## Slide 31: Performance evaluation:
Chart: Execution time normalized to
| stringsearch | qsort | bitcount | crc32 | sha | fft | Average
Original | 100 | 100 | 100 | 100 | 100 | 100 | 100
SWIFT-R | 373.23 | 318.61 | 380.73 | 329.99 | 529.3 | 385.73 | 386.265
nZDC+InCheck | 256.11 | 392.89 | 238.32 | 238.32 | 252.32 | 311.94 | 281.65
386%
281%
nZDC+InCheck programs run 105% faster than SWIFT-R

## Slide 32: Dynamic Instruction breakdown of InCheck+nZDC
Chart: Percentage breakdown of Committed Instructions
| crc32 | bitcount | fft | qsort | sha | stringsearch | Average
nZDC | 68249 | 215325 | 147150 | 54906 | 1786803 | 51985 | 387403
InCheck | 24706 | 31434 | 7478 | 30388 | 373711 | 7646 | 79227.1667

## Slide 33: Future Work:
RTL level fault injection experiments have to be performed to evaluate the effectiveness of InCheck
  Gem5 may not be modeling all the architectural bits accurately
Moving towards formal analysis methods to evaluate InCheck's Fault Tolerance more precisely

## Slide 34: My Publications & Other Projects:
NEMESIS: A Software Approach for Computing in Presence of Soft Errors
  Moslem Didehban, Dheeraj Lokam, Aviral Shrivastava
  *Under review. Submitted to ASPLOS 2017.
InCheck: An Integrated Recovery Methodology for fine-grain Soft Error Detection Approaches
  Dheeraj Lokam, Moslem Didehban, Aviral Shrivastava
    *Submitting to DAC 2017
VeriFi: A Versatile Fault Injection Methodology for an accurate estimation of Soft-Error Resilience
  *Work Under Progress

## Slide 35: Backup Slides

## Slide 36: Fault, Error and Failure
FAULT
a physical defect that
occurs within hw or sw
components
HW defect, SW bug
Physical
Universe
physical entities
making up a system
activation
ERROR
a deviation from accuracy or correctness
manifestation of a fault
Informational
Universe
units of information
(eg: data words)
fault latency
FAILURE
nonperformance of
some action that is due or expected
malfunction
External
Universe
the user of a system
ultimately see the effects
propagation
error latency
[Geffroyand, 02] Jean-Claude Geffroyand Gilles Motet, “Design of Dependable Computing Systems”, KluwerAcademic Publishers, 2002, ISBN 1-4020-0437-0
Notes: Now we like to distinguish faults, soft errors and failures to get rid of naming confusions.

## Slide 37: SWIFT Limitations
Duplicable (Protected)
  Computational and Logical instructions
Non-Duplicable (Unprotected)
  Memory operations and Control Flow instructions
More than 45% of dynamic instructions are non-duplicable

## Slide 38: Statistical Fault Injection
N – Initial Population Size
p – estimated probability of faults resulting in a failure (standard error)
e – margin of error
t – confidence level. Probability that the exact value is actually within the error interval (computed w.r.t Normal distribution)
*Leveugle, Régis, et al. "Statistical fault injection: quantified error and confidence." 2009 Design, Automation & Test in Europe Conference & Exhibition. IEEE, 2009.