## Slide 1: SSDM: Smart Stack Data Management for Software Managed Multicores
Jing Lu
Ke Bai, and Aviral Shrivastava
Compiler Microarchitecture Lab
Arizona State University, USA

## Slide 2: Memory Scaling Challenge
In multi-core processors, , caches provide the illusion of a large unified memory
  Bring required data from wherever into the cache
  Make sure that the application gets the latest copy of the data
Cache coherency protocols do not scale well
  Intel 48-core Single-chip Cloud Computer
  8-core DSP from Texas Instruments, TI 6678
Caches consume too much power
  44% power, and greater than 34 % area
Intel 48 core chip

## Slide 3: SPM based Multicore Architecture
Data Array
Tag Array
Tag Comparators, Muxes
Address Decoder
Cache
SPM
Scratchpad Memory
  Fast and low-power memory close to the core
  30% less area and power than direct mapped cache of the same effective capacity
SPM based Multicore
  A truly distributed memory architecture on-a-chip
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Execution Core
SPM
Interconnect Bus
DMA

## Slide 4: Need for Data Management
Programmability
  Restructuring of existing applications
    Transferring data in and out of the local scratchpad memory
  Programmers need to be aware of :
    Local memory availability
    Task requirement at every point of time
Portability of the application
  Applications are tuned for specific hardware
int global;
f1(){
int a,b;
global = a + b;
f2();
}
int global;
f1(){
int a,b;
DMA.fetch(global)
global = a + b;
DMA.writeback(global)
DMA.fetch(f2)
f2();
}

## Slide 5: Manage Stack Data
Local scratchpad memory is shard between
  Code
  Heap data
  Stack data
  Global data
Important to have approaches to manage stack data
  64% of all accesses in embedded applications are to stack variables
Stack management is difficult
  ‘liveness’ depends on call path
  Function stack size is known at compilation time, but not stack depth
code
global
stack
heap

## Slide 6: State Of Art: Circular Stack Management
Ke Bai et.al., "Stack Data Management for Limited Local Memory (LLM) Multi-core Processors", ASAP, 2011.
Function | Frame Size (bytes)
main | 28
F1 | 40
F2 | 60
F3 | 54
main
F1
F2
F3
main
F1
F2
Stack Size = 128 bytes
28
68
128
SP
F3
Stack region
in Local Memory
Stack region
in Global Memory
GM_SP
Need to be evicted

## Slide 7: Challenge of Stack Data Management
Not performing management when not absolutely needed
  fewer DMA calls
    memory latency of a task will be very strongly dependent on the number of memory requests
Performing minimal work each time management is performed
  Transfer stack data at the whole stack space granularity
    management library (_sstore and _sload) becomes simpler
Avoiding thrashing
  Place management functions judiciously

## Slide 8: Contributions of This Paper
.c
Runtime
Library .a
Weighted Call Graph
compiler
Executable
SSDM
Place info about where to perform management
formulate the optimization problem of where to insert the management functions so as to minimize the management overhead
  Finding an optimal cutting of a weighted call graph
10
5
50
25
F0
32
F1
128
F2
32
F3
20
F4
32
Cut 1
Cut 0
Cut 0
Cut 0
A new runtime library with less management complexity
An effective heuristic (SSDM)
  Takes Weighted Call Graph as input
  Generates an effective management function placement scheme

## Slide 9: Reduction of Management Overhead
Chart: 
| BasicMath | Dijkstra | FFT | FFT_inverse | SHA | String_Search | Susan_Edges | Susan_Smoothing | Average
SSDM | 0 | 0.0089723 | 0.0010279 | 0.001267 | 0.020432 | 0.03007 | 0.00094761 | 0.0024773 | 0.0081492
CSM | 0.099993 | 0.18968 | 0.13306 | 0.13722 | 0.13492 | 0.10525 | 0.077341 | 0.028125 | 0.1132

## Slide 10: Improvement of Overall Performance
Chart: 
| BasicMath | Dijkstra | FFT | FFT_inverse | SHA | String_Search | Susan_Edges | Susan_Smoothing | Average
ILP | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
SSDM | 1 | 1 | 1 | 1 | 1.0011 | 1 | 1 | 1 | 1
CSM | 1.1 | 1.1791 | 1.1319 | 1.1358 | 1.1134 | 1.073 | 1.0763 | 1.0256 | 1.1053

## Slide 11: Summary
Scaling the memory hierarchy is becoming more and more challenging as we scale the number of cores in each processor
One promising solution: scratchpad
  Does not have data management implemented in hardware
  Data management needs to be performed in software
Important to have approaches to manage stack data
  64% of all accesses in embedded applications are to stack variables
Contributions of this paper:
  1. Problem formulation
  2. New runtime stack data management library
  2. Efficient heuristic for stack data management
Reduce stack data management overhead by 13X over the state-of-the-art