## Slide 1: Timestamp Temporal Logic (TTL) for Testing the Timing of Cyber-Physical Systems
MOHAMMADREZA MEHRABIAN, MOHAMMAD KHAYATIAN, AVIRAL SHRIVASTAVA, Arizona State University
JOHN C. EIDSON, University of California Berkeley
PATRICIA DERLER, HUGO A. ANDRADE, National Instruments
YA-SHIAN LI-BABOUD, EDWARD GRIFFOR, National Institute of Standard and Technology (NIST)
MARC WEISS, Marc Weiss Consulting
KEVIN STANTON, Intel corporation
EMSoft 2017

## Slide 2: CPS: Exciting times
Sensors  sensor networks
Embedded systems  networked embedded systems
Control has come to software
  Mechanical  Electrical  computer
The real question for our times is:
If I can sense anything, and I can control everything, what (good) can I do?
Nexus of CPS, Machine Learning and Big Data
  Enable large scale and compelling applications
  Autonomous cars, Smart cities, City-level traffic management, Smart grid

## Slide 3: Timing is fundamental to CPS
Tight sense-compute-actuation loop
Hard-real-time CPS
  correctness depends on functionality as well as correct timing
  autonomous cars
Safety-critical CPS
  failure of timing can lead to a catastrophe or even a disaster!!
Timing constraints come from
  System stability requirements
  System performance requirements
  Legal requirements

## Slide 4: But how can we specify timing constraints?
LTL (Linear Temporal Logic)
  Deals with discrete sequence of states
  Based on logic operators (¬, ∧, ∨), and temporal operators, next (N), always (G), eventually (F), and until (U).
  Boolean predicates, discrete time
  Example constraint: G (r => F g)
  Not sufficient for CPS – CPS operate in continuous time.
MTL (Metric Temporal Logic)
  Boolean predicates, real-time
  Example constraint: G (r => F[0,5] g)
  Not sufficient for CPS – CPS may have real-valued logic

## Slide 5: STL – Signal Temporal Logic
Predicates over real value, real-time
  Assume signals x1[t], x2[t], ..., xn[t], then atomic predicates are of the form: μ = f(x1[t],...,xn[t]) > 0
Example: Between 2s and 6s the signal is between -2 and 2

## Slide 6: Express timing constraints in STL
Intuitive to specify value-based (level-based) timing constraints
  Example: the value of x[t] is less than 2
  φ := G[2,6] (|x[t]| < 2)
Hard to express event-based (edge-based) timing constraints
  Example: Whenever signal x1 rises above 0.5, signal x2 should rise above 0.6 within 1 second
  □ (↑(x1>0.5) ⇒ (♢[0,1](↑(x2>0.6))))
  □ : Globally, ♢: Eventually, ↑: Rise operator
  Definition of the rise operator
    ↑ψ = (ψ ∧(¬ψS⊤)) ∨ (¬ψ ∧(ψU⊤))
event
time
voltage

## Slide 7: Express timing constraints in STL
Harder to express sequential timing constraints on events – they become nested constraints
  Example: Whenever signal x1 rises above 0.5, signal x2 should rise above 0.6 within 1 second and after that, signal x3 should fall below 0.4 within 5 seconds
  ψ = □ ((↑(x1>0.5)) ⇒ (♢[0,1](↑(x2>0.6)) => (♢[0,5] (↓(x3>0.4)))))
  □ : Globally, ♢: Eventually, ↑: Rise operator, ↓: fall operator
  ↑ψ = (ψ ∧(¬ψS⊤)) ∨ (¬ψ ∧(ψU⊤))
  ↓ψ = (¬ψ ∧(ψS⊤)) ∨ (ψ ∧(¬ψU⊤))
  ψ = □((x1> 0.5) ∧ (¬(x1 > 0.5)S⊤)) ∨ (¬(x1 > 0.5) ∧ ((x1 > 0.5)U⊤))) ⇒ (♢[0,1]((x2 > 0.6) ∧ (¬(x2 > 0.6)S⊤)) ∨ (¬(x2 > 0.6) ∧ ((x2 > 0.6)U⊤)) ⇒ (♢[0,5]((¬(x3 > 0.4) ∧ ((x3 > 0.4)S⊤))) ∨ (((x3 > 0.4) ∧ (¬(x3 > 0.4)U⊤))))))

## Slide 8: Expressing timing constraints in STL
Expressing the acceptable tolerance of the timing constraints will make the constraint expressions even more complicated
  Signals x1 and x2 should rise above 0.5 within 1 millisecond of each other
Event-based timing constraints are quite common in CPS
  Example: Airbag and seatbelt operation during an accident in cars
  After a collision is detected, the seat belt should tighten after at most 20 ms, and simultaneously the airbag must deploy, and then after at most 20 ms, the seat belt should be loosened.
Time | Event
t | Accident
t + 20 ±1ms | Seat belt tighten + airbag deploy
t + 40 ±1ms | Seatbelt loosen

## Slide 9: Timestamp Temporal Logic (TTL)
Simply and intuitively express the event-based timing constraints of distributed CPS
Easier to specify the acceptable tolerance of the timing constraints
  Tolerance of timing and its testing is fundamental to CPS and timing measurement
  There is no perfect measurement system
Systematic methodology to generate the logic for real-time monitoring of the TTL timing constraints

## Slide 10: Event Definition
Event is defined by the triplet <s, v, {, }>
  s – name of the signal
  v – value threshold
  rising, and falling
Example <s1, th1, >, or < s2, th2,>
time
Voltage

## Slide 11: Minimum Latency Constraint
A Minimum Latency constraint expresses that the latency between the occurrence of two events is less than some value (c).
< c

## Slide 12: Maximum Latency Constraint
A Maximum Latency constraint expresses that the latency between the occurrence of two events is greater than some value (c).
> c

## Slide 13: Exact Latency Constraint
An Exact Latency constraint expresses that the latency between the occurrence of two events is equal to some value (c) with some tolerance (ε).
= c ± ε

## Slide 14: Latency Constraint
Latency constraint captures the time difference between the occurrence of two events .
<
>
=

## Slide 15: Simultaneity Constraint
Two or more events refers to satisfaction of two or more conditions at the same time with a maximum tolerance .
time

## Slide 16: Chronological Constraint
Chronological constraint is specified when the occurrence order of events matters.
time

## Slide 17: Frequency Constraint
Frequency constraint captures the time interval between every two consecutive events of a repetitive signal.
time
Voltage

## Slide 18: Phase Constraint
Phase constraint captures the latency between two repetitive signal events that have the same frequency
time
Voltage

## Slide 19: Burst Constraint
Expresses constraints on the number of occurrences (N) of events (<s1, th1, >) in a specified time interval (dk) and then silence for at least (m) time units.
…
Voltage
time

## Slide 20: TTL Syntax
Latency
    ; ;
Frequency
  ( is the period of threshold crossing)
    ; ;
Phase
  ( is the period of threshold crossing of )
  ( is the period of threshold crossing of )

## Slide 21: TTL Syntax
Simultaneity
  (t is the timestamp of an event)
Chronological
    is the minimum latency between the events.
Sporadic
  ( is the minimum time between two consecutive events)
    and are consecutive events on signal , and their timestamps, respectively
Burst
  ( events in duration then time unit in silence)

## Slide 22: TTL Capabilities
Simpler specification of sequential timing constraints
Can express both value-based and event-based timing constraints
  (
Can express constraints that contain absolute time
Complex constraints can be specified
  Burst
Timing tolerance can be specified

## Slide 23: Latency Constraint Monitoring
NaN
Instead of evaluating the value of the using the values of signals s1 and s2 at all times…
.. a timestamp based approach allows us to evaluate the constraint only when there is an event (defined in the constraint) on s1 or s2.
More efficient testing logic

## Slide 24: Generate Logic to Monitor TTL Constraints
Whenever signal rises above 0.5, signal should rise above 0.6 within 1 second:
>
>
>
>
<

## Slide 25: Case Study: Two Synchronized Motors
DC Motor1
Slave Controller
Master Controller
DC Motor2
c-Rio Testbed part1
c-Rio Testbed part2
Testbed
Optical sensor2
Optical sensor1
CPS
Synchronized
by IEEE-1588
Synchronized
by NTP

## Slide 26: Two Synchronized Motors in TTL
>
>
==
==
>
>
<

## Slide 27: Conclusion
Timing is fundamental to CPS
How to specify timing constraints
  LTL, and MTL do not allow for real-valued signals, and expressing event-based timing constraints is hard in STL
Timestamp Temporal Logic (TTL)
  Latency, frequency, phase, simultaneity, chronological, sporadic and burst timing constraints
  Allows for simpler expression of event-based timing constraints, and sequential timing constraints
  Allows for mixed value-based and event-based timing constraints
  Allows for global time in the timing constraints
  Timing tolerances can also be specified.
Systematic methodology to generate the logic for monitoring the TTL timing constraints
Demonstrated on synchronized motors, and simultaneous motion capture case-study.