## Slide 1: Learning-based Modeling and Improving Architectural Reliability
Aviral Shrivastava, Arizona State University, US
Kyoungwoo Lee, Yonsei University, KR
Shail Dave, Arizona State University, US
Hwisoo So, Yonsei University, KR
Jinhyo Jung, Yonsei University, KR
Notes: Hello everyone. Thank you for coming for the learning-oriented reliability improvement session.
I'm Hwisoo So in Yonsei University.
This presentation will deal with the architectural-level reliability modeling and improving with machine learning.

## Slide 2: Efficient Architectural Reliability Improvement
Modeling architectural reliability
Protecting system efficiently
Safe: Less need to be protected
Vulnerable: should be protected
Full-protection for architecture is expensive
How to efficiently improve the architectural reliability?
Full-redundancy
Requires
~ 2x cost
Notes: Let me start with the basic idea of architectural reliability.
Of course, full-protection for architecture is expensive since the cost roughly doubles.
Then, how can we improve the architectural reliability efficiently?
(left) Maybe we can model the reliability of target architecture,
(right) and then we can focus on the vulnerable parts efficiently.

## Slide 3: Machine Learning Can Help Architectural Reliability Modeling
Fundamental methodology: fault injection & result analysis
Accelerating Fault Injection by ML
ML-based resiliency analysis
Trial 1
Trial 2
Trial 3
Trial 4
1
0
0
1
Skipping predictable fault injection trials with ML
Analyzing fault data with ML
1
0
0
1
Fault injection
Result analysis
Exhaustive fault injection is impractical
Statistical fault injection have lower confidence
Huge fault data is hard to analyze
Human-crafted features may be inaccurate
Notes: The fundamental methodology to analyze architectural reliability is fault injection and corresponding fault result analysis. However, exhaustive fault injection for all fault sites is almost impossible, and statistical fault injection suffers from lower confidence.
Also, it is hard to analyze huge amount of fault data manually, and analysis with human-crafted features may be inaccurate.
Here, machine learning can mitigate such challenges.
Machine learning can accelerate fault injection by skipping predictable trials.
Also, machine learning can effectively analyze the huge amounts of fault injection results without human-crafted features.

## Slide 4: Machine Learning Can Help Architectural Reliability Improvement
Alternative of full-redundancy  selective / symptom-based protection
Selective protection
Symptom-based protection
How to distinguish vulnerable parts?
What symptoms should the system use to detect errors?
Vulnerable
Safe
Heuristics / probabilistic methods
Heuristics / probabilistic methods
Alternative)
Learning-oriented methods
Distinguishing vulnerable parts by ML
Suggesting symptoms of errors by ML
Notes: The alternatives of expensive full-protection are selective protection that selectively protects vulnerable parts, and symptom-based protection that catches symptoms of errors.
These schemes rely on heuristics and probabilistic methods to distinguish vulnerable parts and adopting symptoms of errors.
Here, machine learning can be an alternative of heuristics and probabilistic methods.
For example, machine learning can distinguish vulnerable parts for selective protection.
Also, machine learning can provide learning-oriented symptoms for symptom-based protections.

## Slide 5: Machine Learning Can Support Architectural Reliability
Modeling architectural reliability
Protecting system efficiently
Safe: Less need to be protected
Vulnerable: should be protected
Machine learning can help both
Architecture-level reliability analysis
Architecture-level reliability improvenent
Notes: So, the rest of this presentation will introduce recent researches that utilizes machine learning to support architectural reliability analysis and improvement

## Slide 6: Agenda
Learning-based Architectural Reliability Modeling
Learning-based Architectural Reliability Improvement
A. Accelerating Fault Injection by ML
B. ML-based resiliency analysis
Trial 1
Trial 2
Trial 3
Trial 4
1
0
0
1
Skipping predictable fault injection trials by ML
Analyzing fault data with ML
Notes: Now, I want to introduce several examples of learning-oriented architectural reliability modeling.
This part includes accelerating fault injection by machine learning, and machine learning based resiliency analysis.

## Slide 7: 1. Accelerating Fault Injection by ML: A-1) Training Vulnerable Flip-flops
On the Estimation of Complex Circuits Functional Failure Rate by Machine Learning Techniques [Lange ‘19]
  Goal: Estimating functional vulnerability factor of flip-flops with minimum fault injection trials
  Training regression model with
    Features from the flip-flops
    Statistical fault injection with few part of flip-flops
  Accurate prediction of flip-flop-vulnerability using only 20% of data
[Lange '19] Lange, Thomas, et al. On the estimation of complex circuits functional failure rate by machine learning techniques, DSN-S 2019
Flip-flop
Gate-level netlist
Fault injection
Regression model
Train
Predict vulnerability
Flip-flops for fault injection
Unseen flip-flops
Notes: The first example of accelerating fault injection is On the Estimation of Complex Circuits Functional Failure Rate by Machine Learning Techniques.
The goal of this research is to estimate the functional vulnerability factor corresponding to the functional masking effect, for each flip-flop instance, with minimum number of fault injection trials.
(right) So, this research proceeds fault injection only for few part of flip-flops, and trains the regression model with the features of flip-flops and the results of fault injection.
With this regression model, this research estimate the vulnerability factors of unseen flip-flops, that previous fault injection did not cover.
Consequently, this research can accurately predict flip-flop-vulnerability using only 20% data.

## Slide 8: 1. Accelerating Fault Injection by ML: A-2) Predicting Fault Behaviors
Understanding Scale-dependent Soft-error Behavior of Scientific Applications [Kestor ‘18]
  Motivation: In large-scale system, even few fault injections may be slow
    Idea) Collect data at small scale to predict fault behavior at large scale
Fault injection at small scale
Machine learning models with various algorithm
M
M
M
M
M
M
[Kestor '18] Kestor, Gokcen, et al. Understanding scale-dependent soft-error behavior of scientific applications, CCGRID 2018
1 core
2 cores
4 cores
8 cores
Training data
B
Best model
16 cores
…
Test models with FI at small scale
4,096 cores large scale system
Predict
Notes: The second example of accelerating fault injection is Understanding Scale-dependent Soft-error Behavior of Scientific Applications.
Since it is hard to proceed fault injection in large-scale applications, the goal of this research is to collect results of fault injection on small-scale, and to use these results to predict fault behaviors at larger scale.
(figure) For this, this research proceeds fault injection for small number of cores, for example, 1, 2, 4, and 8 cores.
Then, this research generates the machine learning model based on the fault injection, and tests the models with the small-scale system but higher number of cores to find the best model.
Finally, the selected model is used to predict the fault behaviors on the large-scale of up to 4,096 cores.

## Slide 9: 1. ML-based Resiliency Analysis: B-1) Analyzing Huge Amount FI Data
Machine Learning Models for GPU Error Prediction in a Large Scale HPC System [Nie ‘18]
  Goal) Analyzing six-month ECC data to train error occurrence classifier
HPC system (Titan supercomputer)
[Nie '18] Nie, Bin, et al. Machine learning models for GPU error prediction in a large scale HPC system, DSN 2018
GPU
CPU
GPU
CPU
GPU
CPU
…
…
18,688
Six-months
ECC logs of GPUs
      Train with
      Temperature
      Power
      App info
      Error history
Two-class classifier
Turn off ECC of target GPU
If an error is not predicted
Notes: Now, I want to introduce examples of learning-oriented analysis. The first example is Machine learning models for GPU error prediction in a large scale HPC system.
The goal of this research is to analyze huge amounts of error correction code data of GPUs, which is hard to analyze manually.
This research collected 6 months log data of error correction code of GPUs in large-scale HPC system, trained two-class classifier by using temperature, power, app information, and error history as features. the trained model can predict whether the current app has a soft error.
This research utilized this trained model to turn off the ECC on the GPU when the error is not predicted.

## Slide 10: 1. ML-based Resiliency Analysis: B-2) Analyzing Huge Amount FI Data
Using Machine Learning Techniques to Evaluate Multicore Soft Error Reliability [Rosa ‘19]
  Goal) Identifying correlation between FI results and application characteristics
[Rosa '19] da Rosa, Felipe Rocha, et al. Using machine learning techniques to evaluate multicore soft error reliability, IEEE CAS 2019
1.2M fault injection trials
FI on virtual platforms
Several thousands of features from statistics
Pruning with machine learning
50
Top-50 error/failure -related features
Analysis example
More branch
More hang and termination
Less output mismatch
Notes: Another example is Using machine learning techniques to evaluate multicore soft error reliability.
The goal of this research is to find correlation between fault injection results and the application characteristics.
For this, this research proceeds more than one million fault injection on virtual platform such as gem5 and OVPSim, and collects the statistics from the simulation.
Among several thousands of features from statistics, this research punres the features to top-50 error and failure related features, with help of machine learning.
Then, this research identified correlation between fault injection results and application characteristics.
For example, more branch instructions lead to more hang and termination errors, but it reduce the output mismatch errors.

## Slide 11: 1. ML-based Resiliency Analysis: B-3) GATPS (1/2)
Deep Soft Error Propagation Modeling Using Graph Attention Network (GATPS) [Ma '22]
  Goal: predict error-prone critical instructions with ML instead of heuristics
  Considering a program as a graph
    Instructions  Nodes
    Relationships  Edges
0 L1: mov -0x8 (%ebp), %eax
1 sh1 $0x2, %eax
2 add 0x8 (%ebp), %eax
3 mov (%eax), %eax
4 add %eax, -0x4 (%ebp)
5 addl $0x1, -0x8 (%ebp)
6 mov -0x8 (%ebp), %eax
7 cmp 0xc (%ebp), %eax
8 jl L1
9 mov -0x4 ($ebp), %eax
9
Define-use relation
Logical relation
0
1
2
3
4
5
6
7
8
Addressing relation
Branch relation
[Ma '22] Ma, Junchi, et al. Deep Soft Error Propagation Modeling Using Graph Attention Network, Journal of Electronic Testing 2022
Notes: The final example of learning-oriented analysis is Deep Soft Error Propagation Modeling Using Graph Attention Network, GATPS.
The goal of GATPS is to predict error-prone critical instructions by machine learning, instead of heuristics.
(right figure) For this, GAPTS considers a program as a graph, where the instructions are nodes and relationships between the instructions are edges.

## Slide 12: 1. ML-based Resiliency Analysis: B-3) GATPS (2/2)
Deep Soft Error Propagation Modeling Using Graph Attention Network (GATPS) [Ma '22]
  GATPS can predict SDC-prone instructions without human-crafted features
[Ma '22] Ma, Junchi, et al. Deep Soft Error Propagation Modeling Using Graph Attention Network, Journal of Electronic Testing 2022
9
0
1
2
3
4
5
6
7
8
Instruction features
Program graph
Fault injection results
Data collection
Graph computation
Self-attention mechanism
    Silent data corruption (SDC) predictions of instructions
Notes: With the instruction features, aforementioned program graph, and fault injection results, GATPS proceed self-attention mechansim to predict silent data corruotion predictions for instruction. Consequently, GATPS can predict SDC-prone instructions without heuristics.

## Slide 13: Agenda
Learning-based Architectural Reliability Modeling
Learning-based Architectural Reliability Improvement
C. Selective protection
D. Symptom-based protection
How to distinguish vulnerable parts?
What sympoms should the system use to detect errors?
Vulnerable
Safe
Notes: Now, I want to introduce examples of learning-oriented reliability improvement.
For your reminder, two categories are the selective protection and the symptom-based protection.

## Slide 14: 2. ML-based Selective Protection: C-1) IPAS (1/2)
IPAS: Intelligent Protection against Silent Output Corruption in Scientific Applications [Laguna '16]
  IPAS distinguishes critical instructions based on two main observations
Observation 1
Observation 2
Most of data corruption errors are acceptable in HPC applications Example) molecular dynamics code
Most scientific applications allow algorithmic verification Example) FFT
Fault
Fault
Silent output corruption (Should be prevented)
Similar output (Acceptable)
Fault-free result
Faulty result
L-2 norm > threshold?
Acceptable
SOC
Y
N
[Laguna '16] Laguna, Ignacio, et al. Ipas: Intelligent protection against silent output corruption in scientific applications, CGO 2016
Notes: The first example of selective protection is IPAS: Intelligent Protection against Silent Output Corruption in Scientific Applications.
The goal of IPAS is to distinguish critical instructions based on two observations.
(left) The first observation is that most of the data corruptions in HPC applications are acceptable. For example, in molecular dynamic codes, small movement of molecule can be acceptable if the output is similar. So, we only need to focus on unacceptable faults that induce silent output corruption.
(right) Another observation is that most scientific applications allow algorithmic verification, so that we can decide whether the faulty result is acceptable or not.

## Slide 15: 2. ML-based Selective Protection: C-1) IPAS (2/2)
Goal of IPAS: protecting only SOC-generating instructions
  Idea: Use machine learning to distinguish SOC-generating instructions
Scientific code (target)
Verification routine
Instruction-level fault injection
Features - Instruction type - Basic block info - Function info - # of affected insts
Outputs
Inst. x, <0,1,7,…>, SOC
Inst. y, <2,5,1,…>, NO_SOC
…
Data
SVM classifier: classifies SOC-generating instructions
Training
Input
Output
Protected scientific code that replicates SOC-generating instructions
[Laguna '16] Laguna, Ignacio, et al. Ipas: Intelligent protection against silent output corruption in scientific applications, CGO 2016
Notes: Based on the two observations, IPAS trains machine learning model to distinguish critical instructions.
(Figure) At first, IPAS proceeds instruction-level fault injections and collects the results of fault injection that are verified by verification routine, and the features of the fault-injected-instructions.
By training the SVM classifier with the collected data, IPAS can classify silent output corruption generating instructions, and then IPAS replicates these instructions to detect faults on these instructions.

## Slide 16: 2. ML-based Selective Protection: C-2) Selective Memristor Protection (1/2)
Efficient Identification of Critical Faults in Memristor Crossbars for Deep Neural Networks [Chen '21]
  Protects DNN-mapped memristor crossbars by classifying critical faults (CFs)
    Generating input: exhaustive fault injection is impractical (< 0.1% faults are critical)
Problem solving by gradient ascent
Dataset
Critical faults
Benign faults
Benign faults can be generated by fault injection
[Chen '21] Chen, Ching-Yuan; Chakrabarty, Krishnendu. Efficient identification of critical faults in memristor crossbars for deep neural networks. DATE 2021
Optimization problem: Goal: Finding fault matrix Δ that maximizes misclassification
…
…
…
…
…
…
Permanent fault combination that maximizes misclassification
Notes: The second example of selective protection is Efficient Identification of Critical Faults in Memristor Crossbars for Deep Neural Networks that focuses on the permanent errors on specific architecture, memristor.
This research observed that less than 0.1% faults are critical on DNN-mapped memoristor crossbars. So, exhaustive fault injection to collect critical fault samples is impractical.
Instead, this research forms a problem solver that finds the fault matrix that maximizes the misclassification rates of the DNN-mapped memristors.
Here, each element of fault matrix indicates the fault on the corresponding memristor.
By solving this and mapping the fault matrix to the memristor, this research can generate critical faults input. Benign faults input can be easily generated by fault injections.

## Slide 17: 2. ML-based Selective Protection: C-2) Selective Memristor Protection (2/2)
By generated dataset, critical fault classifier can be trained
  Critical fault classifier can be used to support online fault detector
Dataset
Critical faults
Benign faults
Critical fault classifier
Fault detector of DNN-mapped memristor crossbars
Fault information
Remapping columns with spares when a column has a critical fault
…
…
…
Spare columns
…
…
…
…
…
…
[Chen '21] Chen, Ching-Yuan; Chakrabarty, Krishnendu. Efficient identification of critical faults in memristor crossbars for deep neural networks. DATE 2021
Notes: Then, this research trains the critical fault classifier based on the generated dataset.
This classifier can be used to support the online fault detector of DNN-mapped memristor crossbars.
If the online fault detector detects a fault, the classifier can determine whether the fault is critical.
And system can remap the faulty column with the spare column only if the detected fault is critical.

## Slide 18: 2. ML-based Symptom-based Protection: D-1) EDMN (1/2)
Efficient On-Line Error Detection and Mitigation for Deep Neural Network Accelerators (EDMN) [Schorn '18]
  EDMN detects and mitigates errors on CNN by a small network
Layer 1 output (Convolutional)
Layer 2 output (Convolutional)
Layer N output (Fully connected)
…
Input image
Task result
Σ
Bit-flip
Σ
Feature activation trace
Did the fault change the result?
…
[Schorn '18] Schorn, Christoph, et al. Efficient on-line error detection and mitigation for deep neural network accelerators, SAFECOMP 2018
Notes: Now, I want to introduce examples of learning-oriented symptom-based protection.
The first example is Efficient On-Line Error Detection and Mitigation for Deep Neural Network Accelerators, EDMN.
The goal of EDMN is to detect a fault on CNN by a small network.
For this, EDMN traces feature activation trace, where each element of this trace indicates the sum of intermediate filter results of CNN, so that this trace can represent the activation of each filter.
EDMN proceeds fault injection and collects the feature activation trace and whether the fault changed the final results or not.

## Slide 19: 2. ML-based Symptom-based Protection: D-1) EDMN (2/2)
EDMN is trained by feature activation traces
  EDMN can be used to detect/correct the anomalies of CNN
Feature activation trace
…
Correct result
Critical fault?
…
…
N
Y
Bird
Truck
Data
…
…
…
…
Training
EDMN
argmax
Corrected task result
Critical error detection
CNN (protection target)
Feature activation trace
> threshold
[Schorn '18] Schorn, Christoph, et al. Efficient on-line error detection and mitigation for deep neural network accelerators, SAFECOMP 2018
Notes: Then, this research trains the EDMN with the collected feature activation traces, the criticality of faults, and the original correct results.
Whenever system runs the protection target CNN, system collects the feature activation trace and tests it with EDMN.
If EDMN detects the fault, system will select the corrected results from EDMN instead of faulty result from the CNN.

## Slide 20: 2. ML-based Symptom-based Protection: D-2) WarningNet (1/2)
WarningNet: A Deep Learning Platform for Early Warning of Task Failures under Input Perturbation for Reliable Autonomous Platforms [Lee '20]
  Motivation: input perturbations can degrade performances of neural netowrks
Examples of action detection failures
Noise
Rain
Normalized accuracy of various tasks under additive white gaussian noise (AWGN) and rain
 | PSNR | Image classification | Object detection | Action detection
AWGN | 23.7 | 0.876 | 0.878 | 0.781
Rain | 23.1 | 0.689 | 0.771 | 0.630
AWGN can be considered as random noise
Rain can be considered as structured noise
[Lee '20] Lee, Minah, et al. Warningnet: A deep learning platform for early warning of task failures under input perturbation for reliable autonomous platforms, DAC 2020
Notes: The final example is WarningNet: A Deep Learning Platform for Early Warning of Task Failures under Input Perturbation for Reliable Autonomous Platforms.
The motivation of WarningNet is that input perturbation can degrade the performance of neural networks.
(left) The left table shows the normalized accuracy of various tasks under additive white gaussian noise that is considered as random noise and rain that is considered as structured noise.
(right) The right examples show the action detection failures under noise and rain.

## Slide 21: 2. ML-based Symptom-based Protection: D-2) WarningNet (2/2)
WarningNet provides early warning of input perturbations
  By predicting types of input perbutations and the probability of accuracy drop based on types of perbutations and the tasks
Original
Random
Structured
Random & structured
+
Random / structured
perturbation
WarningNet: can predict the input perturbation of input image
Perturbation type
Task
Labeling
Impact of input perturbation
[Lee '20] Lee, Minah, et al. Warningnet: A deep learning platform for early warning of task failures under input perturbation for reliable autonomous platforms, DAC 2020
Apply noise reduction before the task
If input perturbation is detected
Notes: (left)
To generate input for the classifier, this research generates images under gaussian noise, rain, and both noises.
Then, this research trains WarningNet based on the images with perturbations and the impact of perturbations.
By this, WarningNet classifier can predict the presence of input perturbation, so that the denoising algorithm can be selectively applied prior to the task only if the input perturbation is detected.

## Slide 22: Summary
Vulnerable
Safe
Machine learning can support architectural reliability
Learning-based Reliability Modeling
Learning-based Reliability Improvement
C. Distinguishing vulnerable parts for selective protection
D. Providing learning-oriented symptoms of errors
A. Accelerating fault injection
experiments
B. Analyzing the resiliency by machine learning
1
0
0
Skip
Notes: Consequently, machine learning can support both
(left) architectural reliability analysis with accelerating fault injection and analyzing the resiliency, and
(right) architectural reliability improvement with distinguishing vulnerable parts and providing learning-oriented symptoms
Thank you for listening this presentation.