## Slide 1: REGISTER FILE ORGANIZATION FOR COARSE GRAINED RECONFIGURABLE ARCHITECTURES (CGRAs)
Dipal Saluja
Compiler Microarchitecture Lab,
Arizona State University, Tempe, Arizona, USA

## Slide 2: Need for Power Efficient Computing
Power Efficient Computing Required at:
  Micro-architecture level
  Chip level
  Data Center Level
Accelerators help achieve power efficient computing
  Specialized Hardware for Application Specific Operations
  Improve performance while reducing power
  Scales from mobile devices to super computers
    Qualcomm’s Adreno
    Titan at Oak Ridge National Laboratory (NVIDIA Tesla)

## Slide 3: Coarse-Grained Reconfigurable Architectures (CGRAs)
2D array of Processing Elements (PEs)
ALU + Local register file → PE
Mesh interconnection
Shared data bus
  Data memory
PE inputs:
  4 Neighboring PEs
  Output Register (Self)
  Local register file

## Slide 4
a
b
c
d
e
f
g
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Time
0
1
2
3
a
b
b
c
d
e
f
g
4
a
b
c
d
e
f
g
What to Map and How?
Notes: CPU: 7cycles, cgra: 4 cycles: modulo: every 2 cycles

## Slide 5
What to Map and How?
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
1
2
3
4
Time
0
1
2
3
4
5
b
c
d
e
f
g
a
a
b
c
d
f
e
g
b
a
b
c
d
f
e
b
g
a
b
c
d
b
2
j+1
J+2
j
II is the performance metric

## Slide 6: Comparison with GPUs and FPGAs
GPGPU | FPGA | CGRA
Data Parallel Loops | Data Parallel Loops | Data Parallel Loops
Non-Parallel Loops | Non-Parallel Loops | Non-Parallel Loops
Setup Time | Setup Time | Setup Time
Notes: Issue column and rating table

## Slide 7: Mapping w/o and with Registers
P
1
2
Q
1
2
P
1
2
Q
1
2
P
1
2
Q
1
2
P
1
2
Q
1
2
P
1
2
Q
1
2
P
1
2
Q
1
2
P
1
2
Q
1
2
P
1
2
Q
1
2
a
b
c
d
Time
1
2
3
4
a
b
c
d
a
b
c
d
a
a
a
a
a
a
a
b
4
2
a
Register utilization decreases II
P
1
2
Q
1
2
for(…)
{
a=1;
b=a-1;
c=b*2;
d=c-a;
}

## Slide 8: Rotating Register File Structure
Rotation performed every II cycles
Proposed in [Essen et al.]
Divide by II
clock
Increment every II cycles
Offset Counter
Modulo #regs Counter

## Slide 9: Rotating Register File in Action
Rotation performed every II cycles
P
1
2
Q
1
2
P
1
2
Q
1
2
P
1
2
Q
1
2
P
1
2
Q
1
2
a
a
a
a
b
c
d
a
a
b
a
2
0
0
0
1
1
1

## Slide 10: Introduction to the Problem
Loop kernels have constants
  E.g., global variables, base address of arrays
Constants are difficult to propagate using Rotating Registers
We need both Rotating RF, as well as Non-Rotating RF in CGRA
My Question:
What kind of structures should we use to support both kind of RFs for CGRAs?
How to efficiently utilize these structures in the compiler?
  Fixed RF
  Shared RF
  Programmable RF

## Slide 11: State of the Art in RF Organizations for CGRA
Most work has explored how to use Rotating RFs in the CGRA
  Architecture: RaPiD [Ebeling et al.] , ADRES [Bouwens et al.]
  Compiler: EMS [Hynchul et al.], [Sutter et al.], REGIMap [Hamzeh et al.]
Hardware impact of Shared Register File configurations studied in [Essen et al., Kwok et al.] in terms of
  Degree of connectivity, Number of ports, Number of registers in the RF
  Estimate the power, area and frequency of the designs
Compilation for Hybrid Architecture (with rotating and non-rotating RF) is largely overlooked

## Slide 12: Fixed RF (FRF): Architecture
Physically partitioned into Rotating and Non-Rotating Region

## Slide 13: Shared RF: Architecture
Rotating Registers per PE and Shared Non-Rotating Registers/Row

## Slide 14: Pros and Cons of each RF Structure
Shared RF | Fixed RF
Partition Fixed at design time | Partition Fixed at design time
Does not scale with the size of CGRA | Scales with the size of CGRA
Limited to 1 write/cycle/row | All PEs in a row can write to their local RF
Increase in Instruction Size | No increase in Instruction Size
High Area and Frequency Overhead | Low Area and Frequency Overhead
Desired RF
Partition Reconfigurable at run-time
Scales with the size of CGRA
All PEs in a row can write to their local RF
No increase in Instruction Size
Minimal Area and Frequency Overhead
Notes: Global RF Partitioning
Local RF Partitioning
Scalability
Write Access to

## Slide 15: Increase in Instruction Size
Fixed RF
  PEs input limited to neighbors, local RF and itself
  No increase in Instruction word size
Shared RF
  PEs now also read from a Shared RF
  Need new bits in Instruction word to read from Shared RF
  Increase in Instruction word size

## Slide 16: Programmable RF (PRF): Architecture
Logical boundary between Rotating and Non-Rotating Region
T
T
T

## Slide 17: Pros and Cons of each RF Structure
Shared RF | Fixed RF
Partition Fixed at design time | Partition Fixed at design time
Does not scale with the size of CGRA | Scales with the size of CGRA
Limited to 1 write/cycle/row | All PEs in a row can write to their local RF
Increase in Instruction Size | No increase in Instruction Size
No configuration instructions needed | No configuration instructions needed
Maximum Area and Frequency Overhead | Least Area and Frequency overhead
1 instance of a variable amongst PEs in the same row. | Multiple copies of the same variable amongst PEs in the same row
Programmable RF
Reconfigurable at run-time
Scales with the size of CGRA
All PEs in a row can write to their local RF
No increase in Instruction Size
1 configuration instruction/PE introduced
Minimal Area and Frequency Overhead
Multiple copies of the same variable amongst PEs in the same row
Notes: Global RF Partitioning
Local RF Partitioning
Scalability
Write Access to

## Slide 18: Compiler Support
for(…)
{
l=p1[i];
a[i]=l+d[i-2];
b=a[i]+1;
c=b-1;
d[i]=a[i]-c;
p2[i]=d[i];
}
a
b
c
d
l
s
2
DFG contains:
Nodes:
  Operation being performed
  Type of operation [Arithmetic, Memory, Constant Operand]
Weighted Edges:
  Depict data dependencies
  Weight signifies loop carried dependency distance

## Slide 19: Compiler Support
Easily integrates with any Mapping Algorithm.
Input: Kernel DFG and CGRA configuration
Output: A Valid Mapping of operations from the Input DFG to a Time Extended CGRA
Steps:
  do{
    mapping = getMapping (DFG, CGRA)
    CheckRFconstraints(mapping, CGRA)
    if(RF Constraints violated)
      MappingNotFound
  }while(MappingNotFound);

## Slide 20: Compiler Support
CheckRFconstraints(mapping, CGRA)
{
RFconstraintsSatisfied = true;
for each operation op in mapping
{
pe_number = op.getMappedPE()
usesRF = op.isRFUsed()
if(usesRF)
{
usesNRF = op.isNRFUsed()
writeToRegister = op.performRegisterWrite();
RFconstraintsSatisfied = CheckPRFconstraints(pe_number, usesNRF, writeToRegister)
}
if(RFconstraintsSatisfied == false)
break;
}
return RFconstraintsSatisfied ;
}

## Slide 21: Compiler Support
    CheckPRFconstraints(pe_number:int, usesNRF:boolean, writeToRegister:boolean)
    {
    if(writeToRegister == true)
    {
    if(PE[pe_number].utilizedRegisters >= CGRA.registersPerPE)
    return false;
    else
    PE[pe_number].utilizedRegisters++
    }
    else //read from RF
    {
    if(usesNRF == false) //uses Rotating RF
    PE[pe_number].utilizedRegisters--
    }
    return true;
    }

## Slide 22: PRF is Best in a Register-Constrained CGRA (Lower II is better)
Chart: Initiation Interval (II)
| band_lin_eq | first_diff | first_sum | hydro_1d | iccg | inner_prod | mat_x_mat | tridiag_elim
PRF | 5 | 5 | 5 | 5 | 9 | 4 | 6 | 5
SNRRF | 5 | 5 | 5 | 5 | 8 | 4 | 6 | 5
FRF | 5 | 5 | 5 | 6 | 8 | 4 | 6 | 5
Chart: II
| band_lin_eq | first_diff | first_sum | hydro_1d | iccg | inner_prod | mat_x_mat | tridiag_elim
PRF | 5 | 5 | 5 | 6 | 9 | 5 | 8 | 5
SNRRF | 5 | 5 | 5 | 0 | 0 | 5 | 0 | 6
FRF | 5 | 5 | 5 | 0 | 0 | 5 | 0 | 7
Mapping with 64 Registers
Mapping with 32 Registers

## Slide 23: PRF Requires the Minimum no. of Registers to get a Mapping
Chart: Number of Registers
| band_lin_eq | first_diff | first_sum | hydro_1d | iccg | inner_prod | mat_x_mat | tridiag_elim | average
PRF | 16 | 16 | 16 | 32 | 32 | 16 | 32 | 16 | 22
SNRRF | 32 | 32 | 32 | 36 | 40 | 28 | 36 | 32 | 33.5
FRF | 32 | 32 | 32 | 64 | 64 | 32 | 64 | 32 | 44

## Slide 24: Number of registers required to achieve the minimum II
Chart: Number of Registers
| band_lin_eq(5) | first_diff(5) | first_sum(5) | hydro_1d(5) | iccg(8) | inner_prod(4) | mat_x_mat(6) | tridiag_elim(5) | average
PRF | 32 | 16 | 16 | 64 | 80 | 64 | 64 | 32 | 46
SNRRF | 32 | 32 | 32 | 52 | 60 | 48 | 40 | 48 | 43
FRF | 32 | 32 | 32 | 96 | 64 | 64 | 64 | 64 | 56

## Slide 25: PRF Imposes Minimal Area Overhead
Chart: Area
| FRF(2RR 2NR) | PRF(4) | SNRRF(2RR 8NR)
Area (sq. micro m) | 399729 | 419710 | 425621
Courtesy: Mahdi Hamzeh and Shri Hari

## Slide 26: PRF Imposes Minimal Frequency Overhead
Chart: Frequency
| FRF(2RR 2NR) | PRF(4) | SNRRF(2RR 8NR)
Frequency (MHz) | 374.1115 | 331.1258 | 327.3322
Courtesy: Mahdi Hamzeh and Shri Hari

## Slide 27: Conclusion
Coarse-Grained Reconfigurable Architectures are promising accelerators
  Specially to speedup Non-Parallel Loops
Registers can be used to improve the performance of loops on CGRA
Most existing work focused on Rotating Registers with CGRA
However, both Rotating and Non-Rotating registers are needed for efficient execution of loops on CGRA
Programmable Register File provides the highest flexibility in terms of application mapping to CGRAs
  Flexible partitioning between rotating and non-rotating regions
  Can map with minimal number of registers
  Scalable architecture
  Minimal area and power overhead

## Slide 28: SNRRF CONFIGURATION LIMITS MAPPING